## Slide 1: Virtual Memory
Pavel Kryukov
29.03.2019

## Slide 2: Layers of Abstraction in Computer Science
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture

## Slide 3: Agenda
Refresher on OS course: virtual memory
Page table
TLB
Virtual-memory related HW optimizations

## Slide 4: Refresher: Virtual Memory

## Slide 5: Refresher: Memory managing
address N
address 0
Initially, resources was managed manually by SW developer
  One program (= process) occupied the whole machine recourses
  There was no “external” programs with unknown code/requirements
Modern requirements
  Multi-tasking → not effective to give all resources to one process
  Many SW → cannot plan their co-existents anymore
How multiple process share the memory?
  What happens if a process tries to access memory of another process?
  What happens if processes need more memory and there is no free one?
  What happens if a new process is spawned?
Process A
Process B
Process C

## Slide 6: Refresher: Virtual Memory
Isolation between processes
  Processes can concurrently run on a single machine
  VM prevents them from illegal accessing the memory of one another
  Allows convenient sharing of memory for communication when required
Illusion of large memory for each process
  VM size can be bigger than physical memory size
  VM decouples program from real size (can differ across machines)
Contiguous memory illusion
  Programmers need not worry about where data is placed exactly
Dynamic growth
  Can add memory to processes at runtime as needed
Over commitment
  Sum of VM spaces (across all processes) can be >> physical space
  Memory often one of the most costly parts in the system

## Slide 7: Virtual and Physical Address Space
Virtual address space
  Space used by the programmer (part of program visible state)
  Perfect abstraction = contiguous and completely belongs to the process
  Physical address space
  The real physical memory (e.g., DRAM) available in the computer
  Not known by the programmer (completely hidden by OS/HW)
  How to map virtual space to physical one?

## Slide 8: Basic Idea of VM
  Split both virtual and physical spaces into fixed size blocks called pages (commonly 4KB)
  Not need to place the whole virtual space into the computer → only pages used by the process
  Pages can be in physical memory or disk
  Memory acts as a cache for the secondary storage (disk)
  Process may use more pages that physical memory can keep
  Each process can access only their pages
Virtual Space
Physical Space
#page
#page
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
2 | 
19 | 
40 | 
41 | 
Disk
#page
60 | 
122 | 

## Slide 9: Page Table

## Slide 10: Page Table
  To perform translation of virtual address into physical one, the special structure called Page Table (PT) is used
  It contains the following information for each page:
  Whether the page is in memory or on the disc
  Physical address of the page (if it is in memory)
  Was its data modified? → need for evictions
  Access rights (read-only, read-write, etc.) → security
  Each process has its own PT
  HW uses PT to translate addresses
  But, all complex tasks (initialization, misses, evictions, etc.) are performed by OS

## Slide 11: Translation
 | Disc or memory? | Modified? | Access Rights? | Physical page number
0 |  |  |  | 
1 |  |  |  | 
… |  |  |  | 
… |  |  |  | 
 | Disc or memory? | Modified? | Access Rights? | Physical page number
0 |  |  |  | 
1 |  |  |  | 
… |  |  |  | 
… |  |  |  | 
Page Table
63 | 11 | 0
Virtual Page Number | Page Offset | 
Virtual Address
31 | 11 | 0
Physical Page Number | Page Offset | 
Physical Address

## Slide 12: Page table structure
Page table implementation is defined by OS
Usually it is a multi-level table
Accessing of final page table entry is a chain of loads (“walk”)
29.03.2019
MIPT-MIPS 2018
63 | 11 | 0
Virtual Page Number | Page Offset | 
31 | 11 | 0
Physical Page Number | Page Offset | 
 | Level 1 Table
0 | 
1 | 
… | 
… | 
 | Level 1 Table
0 | 
1 | 
… | 
… | 
 | Level 2 Table
0 | 
1 | 
… | 
… | 
 | Level 2 Table
0 | 
1 | 
… | 
… | 
 | Level N Table
0 | 
1 | 
… | 
… | 
 | Level N Table
0 | 
1 | 
… | 
… | 
...

## Slide 13: Page fault
Page fault is inability to translate address
  Control is given to OS to perform action, like in exception case
If page is on disk, OS loads page to memory and adds PT entry
If page was not allocated, segmentation fault exception is raised

## Slide 14: Context protection
One process must not access physical memory of another process
  Each process has its own page table therefore
How to write to PT? CPU works in 2 modes at least
Kernel mode:
  entered by syscall
  has write access to PT
  knows what physical addresses are
User mode:
  return from kernel mode by eret instruction
  operates only with own PT in a read-only manner

## Slide 15: Translation Lookaside Buffer

## Slide 16: TLB
  The PT is too huge to be in HW → it is stored in memory
  There are multiple methods to compact it
  Each translation requires several memory accesses
  Needed for every load or store → too many!
  Data cache helps, but not much
  TLB caches recently used PT entries
  speed up translation
  typically 64 to 256 entries
  usually 2 to 8 way associative
  TLB access time is faster than L1 cache access time
Yes
No
TLB Hit ?
Access
Page Table
Virtual Address
Physical
Addresses
TLB Access

## Slide 17: PT, TLB and Cache
Yes
No
Access
TLB
Access
Page Table
In Memory
Virtual Address
Physical
Addresses
TLB
Hit ?
L2 Cache
Hit ?
No
L1 Cache
Hit ?
Yes
No
Data
No
Access
Memory
L2 Cache
Hit ?
Access
Cache

## Slide 18: Handling TLB miss
MIPS traditionally handles TLB miss by software:
  Exception is raised, control is given to OS
  OS fetches PT entry and fills it contents to TLB
x86 does it with hardware
RISC-V allows both

## Slide 19: TLB Protection
Simplest solution — flush TLB on context switch
  Not optimal if “new” context switches back early
Performance-friendly solution — process id is a part of TLB tag
  Translate for different contexts simultaneously
  Safe, one context will not read TLB entries of other contexts

## Slide 20: Vulnerabilities
Speculation and context protection are self-contradicting
  Leads to vulnerabilities like Meltdown or TLBleed
  lw $r1, 0x0($r2) # attempts to read kernel-space memory # raises exception at retirement
  andi $r1, $r1, 0x1 # read bit 0 (may be any)
  slli $r1, $r1, 0x40 # get a cache line offset
  addi $r3, $r3, $r1 # speculatively fetch data to cache # on [$r3] or [$r3 + 0x40]
  // ...
  lw $r4, 0x0($r3) # measure time of instruction to check if cache # miss or hit

## Slide 21: HW optimizations

## Slide 22: Optimization 1: overlapped TLB & cache access
#Set is contained within the Page Offset
  The #Set is known immediately
  Cache can be accessed in parallel with address translation
  Once translation is done, match upper bits with tags
Limitation: Cache ≤ (page size × associativity)
Virtual Memory view of a Physical Address
0
Page offset
11
Physical Page Number
38
Cache view of a Physical Address
0
5
disp
tag
set
6

## Slide 23: Optimization 2: virtually-addressed cache
Address translation only done on a cache miss
Problem 1: two virtual pages mapped to the same physical page
    Must not reside in the cache together
    On a cache miss, use a reverse TLB to verify that no other cache line already in the cache mapped to the missed physical address
Problem 2: flush cache on context switch
    Alternatively: add process ID as part of the tag
Cache
TLB
Main
Memory
VA
PA
CPU
data
data

## Slide 24: Open questions: free discussion
What address should be used for store forwarding?
What address space should be used for prefetching logic?

## Slide 25: Thank You