## Slide 1: Single-cycle implementation of MIPS CPU
Igor Smirnov
31 October 2018

## Slide 2: Acknowledgements
These slides contain material developed and copyright by:
Luis Ceze (UW), CS378, L1, L6 and L8

## Slide 3: Layers of Abstraction in Computes Science
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topic of
this lecture

## Slide 4: ISA

## Slide 5: Refresher: ISA
Instruction Set Architecture (ISA) is a precise definition of computer instructions, features and mechanism (procedures, interrupt/exception handler, etc.) and also some structures (registers, memory, etc.)
It can be thought as an agreement between a programmer and an engineer:
What a typical ISA defines
    Data Formats. (Integer, Floating Point, Vector/Packed)
    Instructions. (Operations, encoding, etc.)
    Registers and Memory Organization.
    Interrupts, exceptions, and traps.
    Implementation-Dependent Features. (Memory control, custom features.)
the programmer-visible state
they change the state

## Slide 6: Refresher: MIPS
An example of a RISC processor.
    Designed for easy programming and implementation.
    Short and simple, but fast instructions → programs are larger than others, but run faster.
The main aim was to take advantages of pipelined execution
    Pipeline was not specified in ISA, but ISA developers tried to simplify its implementation in uArch.
Implementations:
    The first one is R2000 (1986)
    Later: R3000A (PlayStation), R4000 (PSP), R5900 (PlayStation 2), etc.
    Currently it is widely used in embedded systems.
One moment MIPS seemed to be overcome Intel IA-32, but it didn’t happen because Intel’s uArch was significantly better and could compensate the drawback of IA-32.
One moment MIPS seemed to be overcome Intel IA-32,, but it didn’t happen because Intel’s uArch was significantly better and could compensate the drawback of IA-32.

## Slide 7: MIPS: Register-To-Register, Three Addresses
MIPS is a register-to-register, or load/store, architecture
  The destination and sources must all be registers
  Special instructions, which we’ll see soon, are needed to access main memory
MIPS uses three-addresses instructions for data manipulation
  Each ALU instruction contains a destination and two sources
  For example, an addition instruction (a = b + c) has the form:
add a, b, c
operands
operation
destination
source 1
source 2

## Slide 8: MIPS Register File
More registers might seem better, but there is a limit to the goodness
  The more register the larger decoders, multiplexers, etc. → larger circuits delays
  Instruction length is affected, as need more space to encode register numbers
MIPS CPU has 32 registers, each of which holds a 32-bit value
  Register addresses are 5 bits long
  The data inputs and outputs are 32-bits wide
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
5b
5b
5b
32b
32b
32b

## Slide 9: MIPS Register Names
MIPS register names begin with a $. There are two naming conventions:
  By number: $0 $1 $2 … $31
  By (mostly) two-character names: $a0-$a3 $s0-$s7 $t0-$t9 $sp $ra
Why so many different registers?
  Not all of them are general purpose registers (GPR)
  There are a lot of special purposes: procedure mechanism, exception/interrupt handling, etc.
In our project mostly GPRs are used: $t and $s
Number | Name
$0 | $zero
$1 | $at
$2, $3 | $v0, $v1
$4 - $7 | $a0 - $a3
$8 - $15 | $t0 - $t7
$16 - $23 | $s0 - $s7
$24, $25 | $t8, $t9
$26, $27 | $k0, $k1
$28 | $gp
$29 | $sp
$30 | $fp
$31 | $ra
Detailed description of each register can be seen by this link

## Slide 10: R-type instructions
Register-to-register (three register operands) arithmetic instructions use the R-type format:
This format includes six different fields:
  op is an operation code that selects a specific action (also defines the format)
  rs and rt are the first and second source registers
  rd is the destination register
  shamt is only used for shift/rotate instructions
  func is used together with op to select an arithmetic instruction
Example:
op
rs
rt
rd
shamt
funct
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
000000| 10001 | 10010 | 01000 | 00000 | 100000
opcode
rs
rt
rd
shamt
funct
add
$s1
$s2
$t0
signed

## Slide 11: Immediate Operands
R-type instructions take data from registers. How does it occur there?
  From the memory (on the next foils)
  From immediate
MIPS allows to specify a immediate value (signed constant), for the second source instead of a register, i.e. instead of rt
  For example: addi $t0, $t1, 4 # $t0 = $t1 + 4
rt field is too small to preset real constants
  5 bits → values from [-16; 15]
Cannot use R-type format to encode such instructions → need a new format

## Slide 12: I-type Format for ALU Instructions
ALU instructions with immediate (two register operands) use the I-type format:
For uniformity, op, rs and rt are in the same positions as in the R-type format
This format includes four different fields:
  rs is a source register (first operand)
  rt is a destination register
  imm is a signed value of the second operand
The immediate can range from -32,768 to +32,767
  But that’s not always enough → need to write to a register by halves
op
rs
rt
imm
6 bits
5 bits
5 bits
16 bits

## Slide 13: I-type Format for Loads/Stores
I-type format is also used for memory operations (load/store) as they are usually have constant memory displacement:
This format includes four different fields:
  rs is a source register, the base of an address for loads and stores
  rt is a source register for stores, but a destination register for loads
  offset is used as an increment to the base to get the address
Examples
for( int i=0; i < L; i++)
{
int v1 = array[i].v1;
int v2 = array[i].v2;
…
}
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
lw $t1, 0x0004($t2) # Read 4B into $t1 from Mem[ Reg[ $t2] + 0004]
sw $t1, 0x0004($t2) # Write 4B from $t1 into Mem[ Reg[ $t2] + 0004]

## Slide 14: I-type Format for Branches
I-type format is also used for branches
The target address is calculated as the end address of the branch (PC+4) plus the displacement encoded in the instruction
This format includes four different fields:
  rs and rt are the first and second source registers
  offset is specified in terms of words instead of bytes:
  target PC = ( PC + 4) + offset << 2
The branch condition is calculated depending on opcode and source values:
  For example, beq write the target address into PC only if its source operands are equal
beq $t1, $t2, L
add $s1, $s0, $0
add $t3, $t1, $t1
L:
add $v1, $v0, $v0
op
rs
rt
offset in words
6 bits
5 bits
5 bits
16 bits

## Slide 15: J-type format
J-type format is used for instructions that do not access any specified register. They are usually unconditional branches (jumps)
Unlike I-type branches, the offset is not added, but change the least bits of PC:
  target PC = ( PC & 0xf0000000 ) | offset << 2
op
offset in words
6 bits
26 bits

## Slide 16: Single-Cycle implementation

## Slide 17: Single-Cycle Implementation of MIPS
Any ISA can be implemented in many different ways
The simplest one is single-cycle implementation:
  All operations are executed strongly sequentially
  Execution of an instruction is not started until the previous one is completely executed (no overlapping)
  All instructions take the same amount of time – a single cycle
For simplicity, only the following instructions will be considered
Arithmetic | add, sub, or, and, addi, subi
Data transfer | lw, sw
Control | beq

## Slide 18: Instruction Execution Cycle
Fetch Instruction by PC
Read registers
Process Calculations
Read/Write
Memory
Write registers
Update PC
Download instruction from the memory using value stored in the program counter (PC) register as an address.
Read values of registers which are pointed by the instruction as their source operands.
Execute an action encoded in the instruction (e.g. addition, subtraction, address calculation, etc.).
Write the result of the calculation into the memory or read the value using the address calculated on the previous step.
Write the result of the calculation or the value read on the previous step into the memory.
Update the program counter to the next instruction:
PC = PC + InstructionLength
Or it is a taken branch then:
PC = PC + InstructionLength + BranchOffset

## Slide 19: Instruction Fetch
The CPU is always in an infinite loop, fetching instructions from memory and executing them
The program counter or PC register holds the address of the current instruction
MIPS instructions are each four bytes long, so the PC should be incremented by four to read the next instruction in sequence
Add
4
Read
address
Instruction [31-0]
Memory
PC

## Slide 20: Executing R-Type Arithmetic Instructions
op
26
31
Read an instruction from the instruction memory by the address in PC
The source registers, specified by instruction fields rs and rt, should be read from the register file
The ALU performs the desired operation
Its result is stored in the destination register, which is specified by field rd of the instruction word
funct
0
5
shamt
6
10
rd
11
15
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [25-21]
I [20-16]
I [15-11]
ALUop
16
20
rt
rs
21
25

## Slide 21: Executing I-type Arithmetic Instructions
I [20-16]
I [15-11]
Read an instruction from the instruction memory by the address in PC
The 1st source register, specified by instruction field rs, should be read from the register file
The signed immediate is extended (from 16 to 32 bits) and directly transferred to ALU
The ALU performs the desired operation
Its result is stored in the destination register, which is specified by field rt of the instruction word
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [25-21]
ALUop
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
I [25-21]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
ALUSrc
R-type
26
31
0
5
6
10
11
15
16
20
op
funct
shamt
rd
rt
rs
21
25
op
imm
rt
rs
I-type
0
1
m
u
x
I [20-16]
I [15-11]
RegDst
Write
register

## Slide 22: Executing I-type Store Instructions
Read an instruction from the instruction memory by the address in PC
The 1st source register (base address), instruction field rs, is read from the register file
The 2nd source register (written value), instruction filed rt, is read from the register file
The signed displacement is extended (from 16 to 32 bits) and directly transferred to ALU
The ALU calculates the effective address
The value is written into the memory by the effective address
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
ALUSrc
RegDst
R-type
26
31
0
5
6
10
11
15
16
20
op
funct
shamt
rd
rt
rs
21
25
op
displ
rt
rs
I-type
Memory
Write
address
MemWrite
Write
data

## Slide 23: Executing I-type Load Instructions
Read an instruction from the instruction memory by the address in PC
The 1st source register (base address), instruction field rs, is read from the register file
The signed displacement is extended (from 16 to 32 bits) and directly transferred to ALU
The ALU calculates the effective address
The value is read from the memory by the effective address
The result is written in the destination register specified by field rt
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Memory
Write
address
Write
data
ALUSrc
MemWrite
RegDst
R-type
26
31
0
5
6
10
11
15
16
20
op
funct
shamt
rd
rt
rs
21
25
op
displ
rt
rs
I-type
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Memory
Write
address
Write
data
Read
address
ALUSrc
MemWrite
RegDst
Read
data
1
0
m
u
x
MemToReg

## Slide 24: Executing I-type Branch Instructions (1)
Read an instruction from the instruction memory by the address in PC
The source registers, specified by fields rs and rt, are be read from the register file
The signed offset is extended (from 16 to 32 bits) and shifted left by 2 (converted from words to bytes)
The address of the instruction after the branch is calculated (= PC + 4)
The target address of the branch is calculated as ((PC + 4) + (offset << 2))
The ALU compares the source operands (does subtraction) and generate the condition code (==, >, <, etc.)
The PC is update by the address of the instruction after the branch or by the target address depending on the branch opcode and the condition code
beq $t1, $t2, -0x0040
PC =
condition
target address
address of the next instruction
? ((PC + 4) + (-0x0040 << 2))
: (PC + 4)
((Reg[$t1] – Reg[$t2]) == 0)
depends on the branch opcode

## Slide 25: Executing I-type Branch Instructions (2)
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
Zero
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 2
ALUSrc
MemWrite
RegDst
MemToReg
0
1
m
u
x
PCSrc
Add
PC
4
Add
R-type
26
31
0
5
6
10
11
15
16
20
op
funct
shamt
rd
rt
rs
21
25
op
offset
rt
rs
I-type
The branch may or may not be taken, depending on the ALU’s Condition Code output (Zero here)

## Slide 26: The Final Single-Cycle Data Path
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
Zero
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 2
Add
Add
PC
4
0
1
m
u
x
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg

## Slide 27: Control Unit
The control unit is responsible for setting all the control signals so that each instruction is executed properly
The control unit needs 12 bits of an instruction
  Six bits make up the instruction opcode
  Six bits come from the instruction func field
It also needs the Conditional Code (“Zero”) output of the ALU
The control unit generates 7 of output, corresponding to the signals mentioned on the data path
Read
address
Instruction [31-0]
Memory
Read
address
Instruction [31-0]
Memory
RegWrite
ALUop
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg
Control
I [31-26]
I [5-0]
CondCode

## Slide 28: Control signal table
sw and beq are the only instructions that do not write any registers
lw and sw are the only instructions that use the constant field. They also depend on the ALU to compute the effective memory address
ALUOp depends on the instructions’ func field
The PCSrc control signal shows if instruction is branch and it is taken
Operation | RegDst | RegWrite | ALUSrc | ALUOp | MemWrite | MemToReg | PCSrc
add | 1 | 1 | 0 | 010 | 0 | 0 | 0
sub | 1 | 1 | 0 | 110 | 0 | 0 | 0
addi | 0 | 1 | 1 | 010 | 0 | 0 | 0
subi | 0 | 1 | 1 | 110 | 0 | 0 | 0
or | 1 | 1 | 0 | 001 | 0 | 0 | 0
lw | 0 | 1 | 1 | 010 | 0 | 1 | 0
sw | X | 0 | 1 | 010 | 1 | X | 0
beq | X | 0 | 0 | 110 | 0 | X | 0/1

## Slide 29: Summary
A datapath contains all the functional units and connections necessary to implement an instruction set architecture
  For our single-cycle implementation, we use two-ported memory, register file, an ALU, some extra adders, and lots of multiplexers.
  MIPS is a 32-bit machine, so most of the buses are 32-bits wide
The control unit tells the datapath what to do, based on the instruction that’s currently being executed
  The discussed processor has seven control signals that regulate the datapath
  The control signals can be generated by a combinational circuit with the instruction’s opcode and func fields as the input

## Slide 30: Simulation

## Slide 31: MIPS Single-Cycle Data Path
RegWrite
ALUop
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg
Control
CondCode
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
Zero
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 2
Add
Add
PC
4
0
1
m
u
x
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg
Fetch
Decode
Execute
Memory
WriteBack
We are not going to model each component (e.g. multiplexer, adder) as it is done in RTL simulator

## Slide 32: Single-Cycle Implementation modeling
void MIPS::run(const string& tr) {
// ... load trace
this->PC = startPC;
for (uint i = 0; i < instr_to_run; ++i) {
uint32 bytes = fetch(); // fetch() { return mem->read(PC); }
FuncInstr instr(bytes);
read_src(instr); // read_src() { instr->v_src1 = rf->read(instr->rs); …}
instr->execute(); // execute_add() { v_dst = v_src1 + v_src2; }
ld_st(instr);
wb(instr); // wb() { rf->write(instr->rd, instr->v_dst); }
PC = update_pc(instr);
}
F
D
E
M
W
class MIPS {
// storages of internal state
RF* rf;
uint32 PC;
Memory* mem;
void ld_st(FuncInstr& inst);
void wb(const FuncInstr& inst);
public:
MIPS();
void run(const string&, uint instr_to_run);
};

## Slide 33: RISC-V

## Slide 34: RISC-V
RISC-V is an modern implementation of RISC architecture
  Evolution of MIPS: “RISC-V is a modern ISA designed with knowledge of what worked, or didn’t work with MIPS”
Designed to be modular
  Has small mandatory “I - Integer” instruction subset
  More subsets can be added on top of it in a modular way
Allow for expansion through a variable-length instruction-encoding scheme
Is open-sourced and actively evolved by community
  First 6 processors designs created within RISC-V project
  Supported by GCC and LLVM
RISC-V: The Free and Open RISC Instruction Set Architecture

## Slide 35: Assignments on RISC-V
Lot’s of opened issues on RISC-V integration available in simulator
  RISC-V ISA support in simulator
  Modular simulator design for easier support of multiple ISAs
  Support of new instructions
  Interrupts/Exceptions
Project wiki well-defined for MIPS
  Next step is a quality documentation of RISC-V main pillars

## Slide 36: Thank You

## Slide 37: RISC-V ISA
Example of MIPS add instruction …..
Example of RISCV add instruction