## Slide 1: TLP – part 1
Kirill Korolev
30.03.2020

## Slide 2: Motivation
Superscalar is hard to scale:
  ILP is depleted – all independent instruction are already executed in parallel
  Inefficient – power & area grows faster than performance
Alternative way to use area is Multicore:
  1 big core - 6x area with 3x performance
  3 small cores (2x area & performance each) - 6x area with 6x performance boost in total
  2x efficiency!

## Slide 3: Thread-level parallelism
Running tasks can be separated into independent execution threads
  multiple applications running simultaneously
  from a single application – parallelized by a programmer
Single-core CPU utilizes instruction-level parallelism (ILP) of 1 thread
Multicore utilizes thread-level parallelism (TLP)
  Each thread is executed on single core

## Slide 4: Types of multiprocessors
All processors works with one address space
SMP — Symmetric Multi Processing
  Identical processing units with a single shared memory
  Fast and effective memory usage
  Low scalability due to lots of interconnections and limited memory throughput
NUMA — Non Uniform Memory Access
  Each processing unit with its own memory and shared memory bus
  Highly scalable
  Requires special coherency protocols and OS support

## Slide 5: Multiprocessor vs Multicore
Multiprocessor: sharing memory on CPU level
  Original approach
  Good for independent workloads
  Bad for cooperative workloads with data exchange
Multicore: sharing memory between cores of 1 CPU
  More advanced approach on a single chip
  Shared cache and memory bus
  Data exchange through the shared cache
CPU 1
CPU 2
Memory
CPU
core 1
core 2
Cache
Memory

## Slide 6: Memory Coherence in a multicore system
Local
Cache
Core 1
Local
Cache
Core 0
Main Memory
Shared Cache
Each core has its own local cache
  Cores can keep multiple local copies of the same data
  Multiplied data can be damaged if one core modifies it:
[X] ≡ 10
[X] ≡ 20
20
Memory: Mem[X] ≡ 10
Core 0: a = Mem[X] # a = 10
Core 1: Mem[X] = 20
Core 0: b = Mem[X] # b = 10
miss
miss
[X] ≡ 10
hit
Error: read the old value from the local cache
[X] ≡ 10
20
Memory must be coherent:
  All cores must see memory identically
  All cores must see the latest state of memory

## Slide 7: Coherence protocols: MESI
 | Valid? | Owned? | Modified?
Invalid | NO | NA | NA
Shared | YES | NO | NO
Exclusive | YES | YES | NO
Modified | YES | YES | YES
Coherence protocols describe how to handle writes/reads to maintain memory coherence in a multicore system
Example: MESI protocol
  Define 4 states of a cache line
  Describe transactions between states
State rules:
  To modify a line, ownership should be obtained first
  There is no state when a line is modified and contained by other cores

## Slide 8: MESI: example
Local
Cache
Core 1
Local
Cache
Core 0
Main Memory
Shared Cache
[X] ≡ 25
[X] ≡ 35
[X] ≡ 25
[X] ≡ 25
Memory: Mem[X] ≡ 25
Core 0: a = Mem[X] # a = 25
Core 0: Mem[X] ≡ 35
Core 1: b = Mem[X] # b = 35
  Snoop [X]
    Core 0 writeback [X]
Core 1: Mem[X] ≡ 45
  Request ownership for [X]
    Core 0 invalidate [X]
35
[X] ≡ 25
(1, 0)
E
M
35
35
[X]
(1, 1)
S
S
[X]
I
(0, 1)
[X]
M
45

## Slide 9: MESI State Diagram
read shared
read not shared
read
read
read
write
write
write
write
read
write
snoop
request ownership
snoop
snoop
snoop
snoop
request ownership
request ownership
request ownership
request ownership
Shared
Modified
Exclusive
Invalid

## Slide 10: Thank You

## Slide 11: Synchronization
Parallel cooperative tasks with common data require synchronization mechanisms
Synchronization is implemented with atomic operations
  Ability to read and modify memory atomically
  E. g. semaphores, MutEx (mutual exclusion), shared memory
Hardware support: atomic exchange
  Includes 2 special memory instructions: Load Linked and Store Conditional
; exchange R4 and 0(R1):
try: MOV R3, R4
LL R2, 0(R1)
SC R3, 0(R1)
BEQZ R3, try
MOV R4, R2
SC returns 1 to R3 only if 0(R1) was not changed after LL to 0(R1)