## Slide 1: Layers of Computer Architecture
Kirill Korolev
13 September 2021

## Slide 2: What is this course about?
The shortest answer is about Computer Architecture
Computer architecture is the design of the abstraction layers that allow us to implement information processing applications efficiently using available manufacturing technologies
Ok… but what is it?
Application
Physics
Decision: create many layers with standardized interfaces
Issue: the gap is too large to cross it over in one step

## Slide 3: Layer 1: Application
The general tasks: money accounting, text editing, music/video encoding, games etc.
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
Excel
Overwatch
Photoshop

## Slide 4: Layer 2: Algorithms
High-level math methods to perform the task: quick sort, search in graphs, compression, signal encoding etc.
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
JPEG
LZ77
Dijkstra
FFT

## Slide 5: Layer 3: Programming language
Representation of algorithms in formal languages that can be translated to “machine language”
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
C++
Java
Python

## Slide 6: Layer 4: Operating system
Manages computer resources and provides common interface for user programs
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Register-Transfer Level
Circuits
Physics
Linux
FreeBSD
Windows

## Slide 7: Layer 5: Instruction Set Architecture
Definition of “machine language” (commands) and available hardware structures/mechanisms
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Register-Transfer Level
Circuits
Physics
x86
MIPS
RISC-V

## Slide 8: Layer 6: Microarchitecture
High-level definition of hardware structures and operations: caches, buses, registers, pipeline, etc.
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Register-Transfer Level
Circuits
Physics
Core™
Pentium®
Atom®

## Slide 9: Layer 7: Gates/RTL
Detailed definition of hardware: floor plan, wires, signal distribution, etc
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Register-Transfer Level
Circuits
Physics
Latch
XOR
Signal

## Slide 10: Layer 8: Circuits
Structure and operation of base hardware elements: transistors, electricity effects
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Register-Transfer Level
Circuits
Physics
Transistors
Voltage
Current

## Slide 11: Layer 9: Physics
Low level physics effects
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Register-Transfer Level
Circuits
Physics
Semiconductor
Electron
Diffusion

## Slide 12: Layers of Abstraction
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Hardware (HW)
Software (SW)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
HW/SW interface
Computer Science
(CS)
Electrical Engineering
(EE)

## Slide 13: Course focus
We will focus our attention mostly on the microarchitecture, but also look through the ISA and the HW levels
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
The most focus is here

## Slide 14: Performance vs Power vs Cost

## Slide 15: Basic Design Tradeoffs
All three are very important
It is extremely hard to create a feature that improves all factors
Different products (mobile, desktop, etc.) require different balance
Performance
(speed)
Cost
(complexity, area)
Power
(energy consumption and dissipation)

## Slide 16: Performance
What does performance depend on?
Golden rule of CS

## Slide 17: Increasing Performance
How can we increase it?
Better SW: algorithms, optimizations, ISA, etc.
Better design: faster circuits, smaller transistors, etc.
Better uArch: pipelining, caching, prediction, etc.

## Slide 18: Power
Why is power important?
  Less power -> smaller battery -> smaller/cheaper devices
  Less power -> less money for electricity
Power Wall is reached
  Cooling systems cannot dissipate more heat
  We cannot spend more power even if we want
Nuclear reactor? No, power supply for a large data center

## Slide 19: Cost
Fixed Cost (RnD)
    Independent of volume (i.e., number of units made/sold)
    Examples: design time and effort, mask generation, etc.
Variable Cost (manufacturing/production)
    proportional to volume
    Examples: silicon processing, packaging, test
    Most of these related to chip area
The larger chip size the large production cost
    Less chips on one wafer
    Larger probability of error

## Slide 20: Acknowledgements
These slides contain material developed and copyright by:
Krste Asanovic (MIT/UCB), CS152-L1
David M. Koppelman (LSU), EE4720-L1

## Slide 21: Literature
Computer Organization and Design: The Hardware/Software Interface, Patterson D.A., Hennessy J.L., 3rd Edition (Eng) — the main book for this course. It contains all that you need to know about the computer architecture and MIPS ISA.
Computer Architecture: A Quantitative Approach, Hennessy J.L., Patterson D.A., 4th Edition — the classic book about state-of-the-art high-performance computing microarchitectures.

## Slide 22: Thank You