## Slide 1: Внеочередное исполнение команд в современном суперскалярном процессоре
Павел Крюков
15 декабря 2017
pavel.kryukov@phystech.edu

## Slide 2: Superscalar CPU
a CPU that executes 2 or more instructions simultaneously
efficiently extracts instruction level-parallelism (ILP)
F
D
E
M
W
PC
time
4ns
8ns
12ns
16ns
PC + 4
F
D
E
M
W
PC + 8
F
D
E
M
W
F
D
E
M
W
PC + 12
PC + 16
F
D
E
M
W
F
D
E
M
W
PC + 20

## Slide 3: Example: Pentium®
Two pipelines: U and V
  V pipeline is reduced — it can’t execute every instruction
  V pipeline is used only for instruction independent from previous
Instruction decoder decides whether to use V pipeline or not
U-E
U-M
U-W
F
PC
PC + 4
V-E
V-M
V-W
U-M
U-W
D
PC + 8
F
PC + 12
U-E
U-M
U-W
D
PC + 16
F
PC + 20
U-E
D
F
U-E
U-M
U-W
D
V-E
V-M
V-W

## Slide 4: Example: VLIW (Itanium®, E2K)
Compiler merges instructions into bundles
Each bundles is a single instruction for CPU (Very Long Instruction Word)
PC
E1
F
D
W
AGU
M
FP
E2
E1’
FP
E2’
E1
F
D
W
AGU
M
FP
E2
E1’
FP
E2’
PC + 16

## Slide 5: Example: vectorization
Bind independent data to vectors
Each component of vector is processed independently
PC
F
D
W
FP-G
FP-G
FP-B
FP-A
FP-R
FP-B
FP-A
FP-R
F
D
W
FP-G
FP-G
FP-B
FP-A
FP-R
FP-B
FP-A
FP-R
PC + 4

## Slide 6: Problems
Those approachess rarely extract much ILP:
  Subsequent instructions are often dependent
  Vectorization and VLIW introduce many “bubbles”
Solution: out-of-order execution
  Execute instructions based on the “data flow” graph, (rather than program order)
  Still need to keep the visibility of in-order execution

## Slide 7: Data Flow Execution
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r5  r5 + 1
(4) r6  r6 – r3
(5) r4  load [r5 + r6]
(6) r7  r8 * r4
In-order execution
Out-of-order execution
1
3
4
2
5
6
r1
r5
r6
r4
r8
Example:
Data Flow Graph
1
3
4
2
6
5
3
4
6
5
1
2

## Slide 8: Can SW Help?
Parallel algorithms
Sequential hardware
Sequential code (ISA)
The algorithms are parallel and SW sees that parallelism
Initially, HW was very simple: sequential execution, one instruction at a time
There were no need to represent parallelism to HW
Sequential code representation seemed natural and convenient

## Slide 9: Can SW Help?
Sequential hardware
Then, technology allowed building wide and parallel HW, but the code representation had stayed sequential
Decision: extract parallelism back by means of HW only
Due to compatibility still need look like sequential HW
Parallel algorithms
Sequential code (ISA)
Sophisticated
parallel
hardware
Visibility of
sequential HW

## Slide 10: Why Is Order Important?
Many mechanisms rely on original program order and unambiguous architectural state
  Precise exceptions: nothing after instruction caused an exception can be executed
(1) r3  r1 + r2
  (2) r5  r4 / r3
(3) r2  r7 + r6
  Interrupts: need to save the arch state to be able to correctly restart the program lately
(1) r5  Mem[r4]
(2) r3  r1 + r2
(3) r2  r7 + r6
  And others…
  Instructions were executed in the following order: (1) → (3) → (2). Then, (2) led to exception.
  For example, (2) and (3) were executed, but (1) was not. Then, interrupt occurred. From what IP to restart? What to save?
  Where to take old value or r2?
  From what IP to restart? What to save?

## Slide 11: Maintaining Arch State
Solution: support two state, speculative and architectural
Update arch state in program order using special buffer called ROB (reorder buffer) or instruction window
  Instructions written and stored in-order
  Instruction leaves ROB (retired) and update arch state only if it is the oldest one and has been executed
Retirement
Instruction window
Out-of-order execution
Fetch & Decode
Sequential code
Visibility of
sequential execution
Out-of-order
In-order
Legend:
Speculative state
Architectural state

## Slide 12: Dependency Checking
For each source check readiness of its producer
Fetch
Retire
HW instruction window (ROB)
Ready, but not executed
Executes
Legend:
Not ready
?
r3  r1 + r2
r1  …
4
7
1
3
0
5
6
2
8
10
9
11
12
13
14
15
…  r3 + …
r2  …
ready
not ready
.., #15
Src1:
Src2:
Consumers:
  If both sources are ready then instruction is ready
  If a source is not ready, write the instr# into the consumer list of producer
When instruction becomes ready, it says its consumers that their sources become ready too
r3

## Slide 13: How Large Is Window Needed?
In short, the larger window → the better
  Find more independent instructions
  Hide longer latencies (e.g., cache misses, long operations)
Example
  The modern CPU has a window of 200 instructions
  If we want execute 4 instruction per cycle, then we can hide latency of 50 cycles
  It is enough to hide L1 and L2 misses, but not L3 miss (≈200 cycles)
But, there are limitations to find independent instructions in a large window:
  branches and false dependencies

## Slide 14: Limitation: Branches
How to fill a large window from a single sequential instruction stream in presence of branches?
Fetch
Retire
Branch with unknown condition
All subsequent instructions are fetch according to prediction
…
Speculatively fetched instructions can be executed too
Verify the branch prediction
If prediction was wrong, all the subsequent instructions are deleted
deleted
How harmful branches are?
  In average, each 5th instruction is a branch
  Assume accuracy of prediction is 90% (looks high, isn’t it?)
  The probability that 100th instruction in the window will not be removed is (90%)^20 = 12%
Accuracy of branch prediction is very important for Out‑Of‑Order Execution
→ Using branch prediction!
  (e.g., (99%)^20 = 82%)

## Slide 15: Limitation: False dependencies
Need track not only true dependences
Code Example:
1. R1 ← MEM[Addr]
2. R4 ← R1 * R3
3. R1 ← R2 + R3
True dependence (Read-After-Write)
False dependence (Write-After-Write)
1. R1 ← MEM[Addr]
2. R4 ← R1 * R3
1. R1 ← MEM[Addr]
3. R1 ← R2 + R3
Anti-dependence (Write-After-Read)
2. R4 ← R1 * R3
3. R1 ← R2 + R3

## Slide 16: Limitation: False Dependencies
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r5  r5 + 1
(4) r6  r6 – r3
(5) r4  load [r5 + r6]
(6) r7  r8 * r4
Out-of-order execution
Example:
1
3
4
2
6
r1
r5
r6
r4
r8
Data Flow Graph
5
4
3
6
5
1
2
r1
r1
r1
False Dependencies:
Write-After-Write: (1) → (3)
Write-After-Read: (2) → (3)
Significantly decrease performance

## Slide 17: Eliminating False Dependencies
(2) …  ar3 + …
(1) ar3  …
(4) …  ar3 + …
(3) ar3  …
Register name is similar to variable name in a program
  It is just a label to identify dependency among operations
Difference: number of register names is limited by ISA
  It is one of the main reason of false dependencies
HW can contain more registers in the speculative state (i.e. more names) than ISA and perform dynamic register renaming
  Number of registers in arch state is not changed (= ISA)
Requirements
  Producer and all its consumers art renamed to the same speculative register
  Producer writes to the original arch register at retirement
sr10
sr10
sr11
sr11

## Slide 18: Register Renaming Algorithm
Redo register allocation that was done by compiler
Eliminate all false dependencies
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r1  r5 + 1
(4) r6  r6 – r3
(5) r4  load [ r1 + r6 ]
(6) r7  r8 * r4
Example:
Renaming
pr10 ≡ r1
pr11 ≡ r8
pr12 ≡ r1
pr13 ≡ r6
pr14 ≡ r4
pr15 ≡ r7
 | r0 | r1 | r2 | r3 | r4 | r5 | r6 | r7 | r8
pr10
pr11
pr15
pr14
pr12
pr13
pr10
pr10
pr11
pr11
pr12
pr12
pr13
pr13
pr14
pr14
Register Aliases Table (RAT)
pr15

## Slide 19: RAT Restore
Each ROB entry saves previous register alias (history)
On flush, ROB is restores history
(1) r1  r4 / r7
(2) r8  r1 + r2
r1  r5 + 1
jump
(5) r6  r6 – r3
(6) r4  load [ r1 + r6 ]
(7) r7  r8 * r4
Example:
Renaming
pr10 ≡ r1
pr11 ≡ r8
pr12 ≡ r1
pr13 ≡ r6
pr14 ≡ r4
pr15 ≡ r7
 | r0 | r1 | r2 | r3 | r4 | r5 | r6 | r7 | r8
 |  | pr7 |  |  | pr21 |  | pr20 | pr3 | pr8
pr10
pr11
pr15
pr14
pr12
pr13
pr10
pr10
pr11
pr11
pr12
pr12
pr13
pr13
pr14
pr14
Register Aliases Table (RAT)
pr15
r1 was pr7
r8 was pr8
r1 was pr10
r6 was pr20
r4 was pr21
r7 was pr3
History

## Slide 20: Why Is ROB Complex?
The two complex searches though all ROB entries
  At allocation (once per each instruction): to identify producers of the instruction sources
  At scheduling (every cycle): to identify ready instructions and send them to execution
The larger ROB the longer search and large HW structures
  Prevents from doing ROB really large -> loose potential performance
ROB
Out-of-order execution
PRF
EXE
Scheduler
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Memory
Write data
from decoder

## Slide 21: Scheduler Queue
It is enough to check only not completed instructions
  Their number is usually significantly less than ROB size (20-30%)
Decision:
  Create a smaller queue for not completed instructions only (scheduling queue or reservation stations)
ROB
Out-of-order execution
PRF
EXE
Scheduler
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Memory
Write data
from decoder

## Slide 22: Scheduler Queue
Out-of-order execution
It is enough to check only not completed instructions
  Their number is usually significantly less than ROB size (20-30%)
Decision:
  Create a smaller queue for not completed instructions only (scheduling queue or reservation stations)
  All checks (allocation and scheduling) are performed on it
  Use ROB only for order reconstruction at retirement
PRF
EXE
Scheduler
Memory
ROB
SQ
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Write data
from decoder

## Slide 23: SQ Operation Example
 | Dst | Src 1 | Src 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
… |  |  | 
N |  |  | 
Ready?
Producers |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | … | N
Dependency Matrix
Free entries
(1) r1  …
(2) r2  …
(3) …  r1 + r2
1
5
3
r1
…
…
r2
…
…
r2
…
r1
1
1
Example:
At allocation of (3):
Search for Src1 producer
  Found in entry 1
    Mark dependency
Search for Src2 producer
  Found in entry 5
    Mark dependency
At least one is found -> not ready
false

## Slide 24: SQ Operation Example
 | Dst | Src 1 | Src 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
… |  |  | 
N |  |  | 
Ready?
Producers |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | … | N
Dependency Matrix
Free entries
(1) r1  …
(2) r2  …
(3) …  r1 + r2
r1
…
…
r2
…
…
r2
…
r1
1
1
Example:
At completion of (1,2):
Reset dependency to all consumers
For each entry check its readiness
false
true

## Slide 25: Memory Operations Execution
Loads are performed speculatively
  We have to check that load takes correct data
    (1) Mem[r1]  …
    …
    (6) …  Mem[r1]
Stores are never performed speculatively
  There is no transparent way to undo them
Stores are also never re-ordered among themselves
  The store is dispatched only when
    The store has both its address and its data
    There are no older stores awaiting dispatch
Store commits its value to cache post retirement
  If instruction(6) will executes before (1), it will read a wrong value from memory

## Slide 26: Memory Dependencies
OOO Scheduler can track dependency through registers, but not through memory
    (1) Mem[r1]  …
    …
    (6) …  Mem[r1]
Unlike register dependencies, memory dependency cannot be known at allocation
    (1) Mem[r2]  …
    …
    (6) …  Mem[r3]
Decision: load should wait until all the previous stores write into the memory (cache)
It works, but it is too slow (stores write after retirement)
  If instruction(6) will executes before (1), it will read a wrong value from memory
  Registers r2 and r3 can have the same values

## Slide 27: Store Forwarding
Faster decision: load waits only if there is some older store with not calculated address
If addresses of all the previous stores are known and there is no intersection with them, then load can be executed
In case of intersection, the load is waiting until the data of the store is ready
Improvement: load can take data of the overlapping store, it is called Store Forwarding

## Slide 28: Load and Store Buffer
Improvement: load does not wait if there is no overlapping
  Need to wait until all previous stores calculate their address
  Then, check for overlapping
  Fast case: no overlapping → load waits nothing
  Slow case: overlapping → load waits until the closest overlapping store update memory/cache
Store can be at any ROB entry → any entry should be checkable
  To large and slow HW
  On the other hand, not every instruction is load or store
  Like SQ, we can use smaller buffers for stores and loads only (store buffer or SB and load buffer or LB)
  All complex check of the address are done in LB and SB
  ROB just keeps the order of instructions

## Slide 29: SB and LB Operation
(5) …  Mem[r5]
(4) Mem[r4]  …
 | Address | Previous store | Waiting store | Ready?
0 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
… |  |  |  | 
M |  |  |  | 
(3) …  Mem[r3]
(2) Mem[r2]  …
(1) Mem[r1]  …
 | Address
0 | 
1 | 
2 | 
3 | 
… | 
N | 
Store Buffer
…
…
(1) Mem[r1]  …
(2) Mem[r2]  …
(3) …  Mem[r3]
(4) Mem[r4]  …
(5) …  Mem[r5]
Example:
(1)
(2)
(4)
(3)
(5)
NA
NA
NA
NA
1
no
NA
Load Buffer
1
2
no
2
oldest unknown
address: [0x35]
address: [0x01]
address: [0x25]
address: [0x25]
address: [0x35]
[0x25]
[0x01]
[0x25]
[0x35]
[0x35]
[0x25]
OK
yes
[0x35]
NO: (1)
0

## Slide 30: False Dependency from Store Data
If there is no overlapping load does not depend on store data
It depends only on store address
  To know that there is no overlapping load wait until all store addresses are calculated
Address is calculated when store is executed
But, store is sent to execution only all its sources (including data) are ready → there is a false dependency from data
(1) r1  …
(2) r2  …
(3) Mem[r1]  r2
…
(N) …  Mem[r3]
1
2
3
N
r1
r2
address
Example:
Data Flow Graph
  r3 != r1 → (3) and (N) are not overlapped
  False dependency:
  in fact, (N) does not need to wait (2)

## Slide 31: STA and STD
To remove false dependency in case of absence of overlapping store instruction is executed in two steps:
  Store address calculation (STA)
  Store data calculation (STD)
Load is waiting for STD only if it overlapped with STA
(1) r1  …
(2) r2  …
(3) addr  [r1]
(3’) Mem[addr]  r2
…
(N) …  Mem[r3]
1
3
N
r1
addr
Example:
Data Flow Graph
  Exist only if overlapping is detected
STA →
STD →
2
r2
3’
data

## Slide 32: SB and LB Operation: STA and STD
(5) …  Mem[r5]
(4) Mem[r4]  …
 | Address | Previous store | Waiting store | Ready?
0 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
… |  |  |  | 
M |  |  |  | 
(3) …  Mem[r3]
(2) Mem[r2]  …
(1) Mem[r1]  …
 | Address
0 | 
1 | 
2 | 
3 | 
… | 
N | 
Store Buffer
…
…
(1) Mem[r1]  …
(2) Mem[r2]  …
(3) …  Mem[r3]
(4) Mem[r4]  …
(5) …  Mem[r5]
Example:
(1)
(2)
(4)
(3)
(5)
NA
NA
NA
NA
1
no
NA
Load Buffer
1
2
no
2
oldest unknown
address: [0x35]
address: [0x01]
address: [0x25]
address: [0x25]
address: [0x35]
[0x25]
[0x01]
[0x25]
[0x35]
[0x35]
[0x25]
yes
[0x35]
0
Data
data: 0x100
0x100
(1)
yes
hit

## Slide 33: MD speculation
Load waits if there is some older STA with not calculated address
Can we make it faster? Yes, if load was dispatched speculatively
When STA is ready, perform check of all ‘skipped’ loads

## Slide 34: MD speculation prediction
MD speculation requires decision making
The idea is to track history similar to branch prediction
Approach 1:
  assume “unknown” loads as speculative
  if the assumption is wrong, add PC of load to “blacklist”
  big overhead on rollbacks
Approach 2:
  assume “unknown” loads as non-speculative
  if there were no STAs to wait, add PC of load to “whitelist”
  moderate overhead as loads wait STAs in the beginning

## Slide 35: Summary
Modern CPU execute instructions out-of-order
To maintain compatibility, architecture state is maintained
Depth of out-of-order engine is limited:
  by accuracy of branch prediction
  by false dependencies
False dependencies may be eliminated by register renaming
To reduce hardware complexity, scheduling is usually applied
Memory dependencies are tracked in-flight by dedicated buffers. Optimizations are:
  Store forwarding: bypass cache if data can be transferred between registers
  Split to STA/STD: makes loads less dependent from stores
  Memory disambiguation speculation: execute loads earlier speculatively