## Slide 1: ILP. Superscalar. OOO – part 1
Oleg Ladin
15.03.2021

## Slide 2: Parallelism
We started from a simple Single-Cycle implementation
In order to keep all units busy, the Pipelining approach was introduced
  Pipeline exploits Instruction Level Parallelism (ILP)
ILP is Fine-grained parallelism (low level)
  Typically extracted by HW, which is power costly (hazard processing)
  Software-driven ILP extraction has compatibility drawbacks
After pipelining there are several advanced approaches to utilize it
  Superscalar
  VLIW
  Vector CPUs

## Slide 3: Parallelism
There is also Coarse-grained parallelism – Thread-Level Parallelism (TLP)
To achieve the best performance, workload may be parallelized to several threads
  Unlike ILP, TLP is extracted manually by programmer
Threads can be extracted either from:
  The same application
  Different applications running simultaneously
  Operating system services
Details in the next lectures

## Slide 4: Superscalar processors
Single-cycle and pipelined processors are unified to scalar class as they process 1 instruction in 1 cycle
Superscalar CPU processes 2 or more instructions in each cycle with additional pipeline
F
D
E
M
W
PC
time
4ns
8ns
12ns
16ns
PC + 4
F
D
E
M
W
PC + 8
F
D
E
M
W
F
D
E
M
W
PC + 12
PC + 16
F
D
E
M
W
F
D
E
M
W
PC + 20

## Slide 5: Example: dynamic scheduling of Pentium®
2 pipelines: U and V
    V pipeline is reduced — it can’t execute every instruction
    V pipeline is used only for instruction independent from previous
Decoder decides whether to use V pipeline or not
U-E
U-M
U-W
F
PC
PC + 4
time
4ns
8ns
12ns
16ns
V-E
V-M
V-W
U-M
U-W
D
PC + 8
F
PC + 12
U-E
U-M
U-W
D
PC + 16
F
PC + 20
U-E
D
F
U-E
U-M
U-W
D
V-E
V-M
V-W

## Slide 6: Alternative: VLIW (Itanium® and E2K)
Compiler merges independent instructions to “bundles”
Each bundle is a single instruction for CPU (Very Long Instruction Word)
Disadvantages:
  Compiler often adds “nops”
  Delay in one instruction delays whole bundle
PC
E1
F
D
W
AGU
M
FP
E2
E1’
FP
E2’
E1
F
D
W
AGU
M
FP
E2
E1’
FP
E2’
PC + 16

## Slide 7: Alternative: Vectorization
Bind independent data to vectors
Each component of vector is processed independently
Limitation:
  Many instructions are scalar
PC
F
D
W
FP-G
FP-G
FP-B
FP-A
FP-R
FP-B
FP-A
FP-R
F
D
W
FP-G
FP-G
FP-B
FP-A
FP-R
FP-B
FP-A
FP-R
PC + 4

## Slide 8: In-order Superscalar
In-order Superscalar is the evolution of Pipeline
  Need to double HW structures
  Max speedup is 2 instruction per cycle (IPC = 2)
  The real speedup is less due to dependencies and in-order execution
F | D | E | M | W
F | D | E | M | W | 
 | F | D | E | M | W
F | Stall
D | E | M | W | 
F | D | E | M | W
F | D | E | M | W
F | Stall

## Slide 9: Is Superscalar Good Enough?
Theoretically can execute multiple instructions in parallel
  Wider pipeline → more performance
But…
  Only independent subsequent instructions can be executed in parallel
  Whereas subsequent instructions are often dependent
  So, the utilization of the second pipe is often low
Solution: out-of-order execution
  Execute instructions based on the “data flow” graph, (rather than program order)
  Still need to keep the visibility of in-order execution

## Slide 10: Data Flow Execution
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r5  r5 + 1
(4) r6  r6 – r3
(5) r4  load [r5 + r6]
(6) r7  r8 * r4
In-order execution
Out-of-order execution
1
3
4
2
5
6
r1
r5
r6
r4
r8
Example:
Data Flow Graph
1
3
4
2
6
5
3
4
6
5
1
2

## Slide 11: Can SW Help?
The algorithms are parallel, and SW sees that parallelism
Initially, HW was very simple: sequential execution, one instruction at a time
There were no need to represent parallelism to HW
Sequential code representation seemed natural and convenient
Parallel algorithms
Sequential hardware
Sequential code (ISA)

## Slide 12: Can SW Help?
Then, technology allowed building wide and parallel HW, but the code representation had stayed sequential
Decision: extract parallelism back by means of HW only
Due to compatibility still need look like sequential HW
Sequential hardware
Parallel algorithms
Sequential code (ISA)
Sophisticated
parallel
hardware
Visibility of
sequential HW

## Slide 13: Why Is Order Important?
Many mechanisms rely on original program order and unambiguous architectural state
  Precise exceptions: nothing after instruction caused an exception can be executed
(1) r3  r1 + r2
  (2) r5  r4 / r3
(3) r2  r7 + r6
  Interrupts: need to save the arch state to be able to correctly restart the program lately
(1) r5  Mem[r4]
(2) r3  r1 + r2
(3) r2  r7 + r6
  And others…
  Instructions were executed in the following order: (1) → (3) → (2). Then, (2) led to exception.
  For example, (2) and (3) were executed, but (1) was not. Then, interrupt occurred. From what IP to restart? What to save?
  Where to take old value or r2?
  From what IP to restart? What to save?

## Slide 14: Maintaining Arch State
Solution: support two state, speculative and architectural
Update arch state in program order using special buffer called ROB (reorder buffer) or instruction window
  Instructions written and stored in-order
  Instruction leaves ROB (retired) and update arch state only if it is the oldest one and has been executed
Retirement
Instruction window
Out-of-order execution
Fetch & Decode
Sequential code
Visibility of
sequential execution
Out-of-order
In-order
Legend:
Speculative state
Architectural state

## Slide 15: Dependency Checking
For each source check readiness of its producer
  If both sources are ready, then instruction is ready
  If a source is not ready, write the instr# into the consumer list of producer
When instruction becomes ready, it says its consumers that their sources become ready too
Is it enough?
No, need to wait until the previous value of the destination is read by
all consumers.
Is it a real dependency?
– Is it a false dependency.
Fetch
Retire
HW instruction window (ROB)
Ready, but not executed
Executed
Legend:
Not ready
?
r3  r1 + r2
r1  …
4
7
1
3
0
5
6
2
8
10
9
11
12
13
14
15
…  r3 + …
r2  …
ready
not ready
.., #15
Src1:
Src2:
Consumers:
r3

## Slide 16: How Large Is Window Needed?
In short, the larger window → the better
  Find more independent instructions
  Hide longer latencies (e.g., cache misses, long operations)
Example
  The modern CPU has a window of 200 instructions
  If we can execute 4 instruction per cycle, then we can hide latency of 50 cycles
  It is enough to hide L1 and L2 misses, but not L3 miss (≈200 cycles)
But there are limitations to find independent instructions in a large window:
  Branches and false dependencies

## Slide 17: _

## Slide 18: Backup section