## Slide 1: Combinational Circuits
Oleg Ladin
21 September 2020

## Slide 2: Layers of Abstraction in CS
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture

## Slide 3: Boolean operations: Inversion
NOT (Inversion)
x
!x
x | !x
0 | 1
1 | 0
2 MOSFET
Vcc
1
Output
0
x

## Slide 4: Boolean operations: AND & OR
AND (or Boolean multiplication)
NAND
x*y
x
y
x | y | x*y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
!(x*y)
x
y
OR (or Boolean addition)
NOR
x+y
x
y
x | y | x+y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
!(x+y)
x
y
Vcc
1
Output
0
A
B
Vcc
1
Output
0
A
B
4 MOSFET
4 MOSFET

## Slide 5: Boolean functions
Boolean operations can be combined into functions
F(x,y,z) = x + !y*z
x
y
z
x + !y*z
x | y | z | F
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | … | … | 1
0
1
0
0

## Slide 6: Combinational Circuits

## Slide 7: Combinational Circuits
If the output of a function is completely defined by the current input then the function is called combinational :
Qt = F(xt, yt, zt, …)
A lot of things can be implemented using combinational circuits
    e. g. adder, decoder, multiplexer…

## Slide 8: Adder

## Slide 9: Half adder scheme
half +
y
x
sum
carry
It is an adder, but it is not a full adder, because it does not have input carry
 |  | xy | x*y
x | y | sum | carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
It is an adder …but not a full adder
  No input carry
sum = xy = !x*y + x*!y
carry = x*y
carry
x
y
sum

## Slide 10: Full adder scheme
+
yn
xn
sn
cn
cn-1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
It is called a full adder
xn | yn | cn-1 | sn | cn
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
We add input carry here
half +
half +
yn
xn
cn-1
Cn
sn

## Slide 11: Wide adder
cn-1
cn
cn+1
We may add more adders to sum numbers wider than 1 bit
In real HW, wide adders have more complicated schemes to avoid long “carry chains”
+
yn
xn
+
sn
+
+
+
+
+
+
yn+1
xn+1
sn+1

## Slide 12: Subtraction

## Slide 13: Representation of negative numbers
  Goal: use adder HW for both add and sub
  Ones’ complement representation: -x = !x
    (111)
  Symmetric range: to
  2 representations for zero
  Two’s complement representation: -x = !x + 1
  Asymmetric range: to
  1 representation for zero
000
001
111
010
011
101
100
110
+1
-2
+2
0
+1
-1
+3
-4
-3
-2
-0
0

## Slide 14: Example of subtraction
Example: 2 – 3 = ?
  2 – 3 = 2 + (−3)
  2 + (−3) = 010 + 101 = 111
  111 = −1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1

## Slide 15: Overflow
Example: −2 – 3 = ?
  −2 – 3 = −2 + (−3)
  −2 + (−3) = 110 + 101 = 1011
  011 = 3 → Overflow 
Overflow conditions
  negative + negative = positive
  positive + positive = negative
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1
000
001
111
010
011
101
100
110
+1
0
+2
+3
-4
-3
-2
-1