## Slide 1: Integrated Circuits
Oleg Ladin
14 September 2020

## Slide 2: Layers of Abstraction in Computer Science (CS)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture
Less about electrons, semiconductors…
More about voltages, wires and transistors…

## Slide 3: Semiconductors

## Slide 4: Why Transistor?
Transistors are the fundamental building blocks for all digital circuits
The main advantage of transistors over other devices (i.e., vacuum tubes) is that they are:
    Very small (~ 10nm)
    Reliable (the 1946 ENIAC, with over 17,000 vacuum tubes, had a tube failure on average every two days)
    Power efficient (almost don’t consume energy when the state is not changed)
    Cheap (production cost of a processor is about several dollars, but it contains billions of transistors)

## Slide 5: Silicon
Planar structure of silicon crystal
Stick model of a silicon atom
Purified silicon
Silicon (Si) is a chemical element with atomic number 14
It has four electrons in the outermost shell available for covalent chemical bonding:
↑↓
↑↓
↑↓
↑↓
↑↓
↑
↑
↑
↑
Si (+14)

## Slide 6: Conduction properties
Spontaneous electron-ion par creation
Pure silicon is a semiconductor: is doesn’t conduct strong electrical current, because it has few free charge carriers
Silicon dioxide (SiO2) is an insulator: sand doesn’t conduct any electrical current.

## Slide 7: N-type Doping
N-type semiconductor (Si doped by P atoms)
P
P
P
+
-
↑↓
↑↓
↑↓
↑↓
↑↓
↑↓
↑
↑
↑
P (+15)
↑↓
↑↓
↑↓
↑↓
↑↓
↑
↑
↑
↑
Si (+14)
+
-
+
-

## Slide 8: P-type Doping
P-type semiconductor (Si doped by Al atoms)
Al
Al
Al
↑↓
↑↓
↑↓
↑↓
↑↓
↑
↑
↑
↑
Si (+14)
↑↓
↑↓
↑↓
↑↓
↑↓
↑
↑
↑
Al (+13)
+
-
-

## Slide 9: “Holes” concepts
An electron hole is the conceptual and mathematical opposite of an electron. The concept describes the lack of an electron at a position where one could exist in an atom or atomic lattice.
15-puzzle game example:
1
5
12
14
9
3
11
7
8
10
15
4
13
2
6

## Slide 10: MOSFET

## Slide 11: Abstracting From Physics
Real physical circuits deal with physical properties, such as voltages and currents
Digital circuits use the abstractions of 0 and 1 to represent the presence or absence of these physical properties (signals) rather than a continuous range
Logic 1
Logic 0
Weak 1
Weak 0
undefined
5 V
3.5 V
1.5 V
0 V
voltage
It could not be a stable state: should not occur in the circuit except during transitions from one state to he other
Boolean algebra describes two-stated systems
X

## Slide 12: MOSFET
The metal-oxide-semiconductor field-effect transistor (MOSFET) acts as a voltage-controlled switch with three terminals: source, drain, and gate
    The gate controls whether current can pass from source to drain or not
There are two variations of the MOSFET: the n-channel (this slide) and the p-channel
Source
Gate
Drain
+
-
-
-
+
+
+
-
-
-
Metal
Oxide layer
P-type semiconductor
N-type semiconductor

## Slide 13: Diffusion process
Holes and electrons diffuse into the n-type and p-type semiconductors correspondently
The diffusion process creates the balancing field (Ed) that prevents deeper diffusion
Source
Gate
Drain
+
+
+
+
-
-
-
-
-
-
Ed
Ed
Ed
+
+
+
+
-
-
-
-
-
-
Ed
Ed
Ed

## Slide 14: Closed State for N-type MOSFET
For N-type MOSFET if the gate is not connected (high-impedance state, Z) or equal to 0 there is not current through the drain
    One of n-p junction is always closed
Source
Gate
Drain
0/Z
0
Z
Ecc
Ed
This p-n junction is closed: its field balances the field of the supply
No current through this p-n junction

## Slide 15: Open State for N-type MOSFET
For N-type MOSFET if the gate is equal to Vt (Logic 1) then the transistor is open: the source value pass to the drain
The current passes though the small channel created by the gate field (more detailed explanation is out of scope of our course)
Source
Gate
Drain
+
+
+
+
-
-
Vt (==1)
0
0
N-type channel with free conductors (electrons)
Eg

## Slide 16: N-type MOSFET logical scheme
When the gate is “closed”, transistor does not conduct
When the gate is “open”, transistor can conduct “0”
When the gate is “open”, transistor conducts “1”, but:
Source
Gate
Drain
1
1
Voltage between source and gate is 0, so p-n is not fully “open” (details are beyond the scope of our course)
Gate | State | Input (Source) | Output (Drain)
1 | On (conduct) | 0 | 0
 |  | 1 | weak 1
0 (any other value than 1) | Off (not conduct) | any | Z
Gate
Drain
Source

## Slide 17: N and P-type MOSFET
Gate | State | Input (Source) | Output (Drain)
1 | On (conduct) | 0 | 0
 |  | 1 | weak 1
0 (any other value than 1) | Off (not conduct) | any | Z
Gate
Drain
Source
Gate | State | Input (Source) | Output (Drain)
0 | On (conduct) | 0 | weak 0
 |  | 1 | 1
1 (any other value than 0) | Off (not conduct) | any | Z
Gate
Drain
Source
N-type MOSFET:
P-type MOSFET (similar to N-type, but all is inverted):

## Slide 18: Invertor
Input | Output
0 | 1
1 | 0
Gate
Drain
Source
Gate
Drain
Source
0
Vcc
1
Input | Output
0 | Z
1 | 0
Input | Output
0 | 1
1 | Z
0
Vcc
1
Input
Output
1
0
Z
The bottom part
The top part
The full scheme
Input
Output
!A

## Slide 19: Thank You