## Slide 1: Pipelining
Igor Smirnov
14 November 2018

## Slide 2: Acknowledgments
These slides contain material developed and copyright by:
Lihu Rappoport (MAMAS/Intel), 234267, L2
Luis Ceze (UW), CS378, L10, L11, L12

## Slide 3: Refresher: MIPS Single-Cycle Implementation
RegWrite
ALUop
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg
Control
Cond Code
Read
address
Instruction [31-0]
Memory
0
1
m
u
x
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
Zero
I [25-21]
I [20-16]
I [15-11]
ALUop
Sign extend
I [15-0]
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 2
Add
Add
PC
4
0
1
m
u
x
ALUSrc
MemWrite
PCSrc
RegDst
MemToReg
Fetch
Decode
Execute
Memory
WriteBack
F
D
E
M
W
2ns
1ns
2ns
2ns
1ns
Fig.: the MIPS main stages

## Slide 4: Drawback of Single-Cycle Implementation
Throughput is 1 instruction per clock (8ns)
Is it efficient?
  Most of the time stages do nothing and just wait until the other stages complete their job
Can we make it faster?
F
D
E
M
W
PC
F
D
E
M
W
PC + 4
F
D
E
M
PC + 8
Sync signal
(clocks)
instructions
time
4ns
8ns
12ns
16ns
– NO!
– YES, with pipelined execution

## Slide 5: What is pipelining?
The main idea: try to keep everyone busy with useful work
  Pipelining is a general-purpose technique of increasing efficiency: it is not specific for processors only
How to organize the pipeline?
  Split the process into independent parts (stages)
  Allow a stage starts execute the next workload event if the following stages are still processing the previous ones
There are many examples of pipelines in the real life
  Assembly line (car, electronics, etc.)
  Security control in an airport

## Slide 6: Processor Pipeline
It is hard to build HW that identifies whether the next stage is busy and stop the pipeline if it is
The alternative is making all stages the same length as the longest one
  It makes the pipeline control easier as the next stage is always ready
Throughput is still 1 instruction per clock, but the clock cycle is 4 times less (2ns vs. 8 ns)
wait
F
D
E
M
W
wait
wait
F
D
E
M
W
wait
wait
F
D
E
M
W
wait
PC
PC + 4
PC + 8
time
4ns
8ns
12ns
16ns
Sync signal
(clocks)

## Slide 7: Pipelined vs. Non-Pipelined MIPS
F
D
E
M
W
PC
F
D
E
M
W
PC + 4
F
D
E
M
PC + 8
instructions
time
Sync signal
(clocks)
4ns
8ns
12ns
16ns
wait
F
D
E
M
W
wait
PC
PC + 4
PC + 8
wait
F
D
E
M
W
wait
wait
F
D
E
M
W
wait
time
Sync signal
(clocks)
4ns
8ns
12ns
16ns
Pipelined
Non-Pipelined

## Slide 8: Pipelining MIPS
PC
<< 2
Add
Add
4
0
1
PCSrc
Memory
0
1
Registers
ALU
ALUop
Sign ext
0
1
Memory
1
0
ALUSrc
MemWrite
RegDst
MemToReg
Control
Memory
RegWrite
Let’s also postpone branches for a separate lecture on control hazards
Let’s postpone the control signals for a while

## Slide 9
PC
Memory
0
1
Registers
ALU
ALUop
Sign ext
0
1
Memory
1
0
ALUSrc
MemWrite
RegDst
MemToReg
Memory
RegWrite
PC is also a pipeline latch, as it separates stages: fetch of the current and the next instructions

## Slide 10: Stages
PC
Memory
0
1
Registers
ALU
ALUop
Sign ext
0
1
Memory
1
0
ALUSrc
MemWrite
RegDst
MemToReg
Memory
RegWrite
PC
Fetch
stage (IF, F)
Decode
stage (ID, D)
Execute
stage (EX, E)
Memory
stage (MEM, M)
Write
Back
stage (WB, W)
Fetch latch (F)

## Slide 11: Pipelined CPU with Control
Instruction
Decode /
register fetch
Instruction
fetch
Execute /
address
calculation
Memory
access
Write
back
ALUSrc
6
ALU
result
Zero
Add
result
Add
Shift
left 2
ALU
Control
ALUOp
RegDst
RegWrite
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
MemRead
MemWrite
Address
Write
Data
Read
Data
Data
Memory
Branch
PCSrc
MemtoReg
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
Control
WB
MEM
WB
MEM
WB
EXE

## Slide 12: Pipelined execution: Load (cycle 1 – Fetch)
op
rs
rt
immediate
0
16
21
26
31
2
1
30
LW
LW R1, (30)R2 ;
6
ALU
result
zero?
result
Add
Shift
left 2
ALU
Control
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
Address
Write
Data
Read
Data
Data
Memory
MemRead
MemWrite
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
ALUSrc
ALUOp
RegDst
RegWrite
Branch
PCSrc
MemtoReg
lw
PC+4
R1  Mem[R2+30]
PC

## Slide 13: Pipelined execution: Load (cycle 2 – Dec)
op
rs
rt
immediate
0
16
21
26
31
2
1
30
LW
LW R1, (30)R2 ;
6
ALU
result
zero?
result
Add
Shift
left 2
ALU
Control
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
Address
Write
Data
Read
Data
Data
Memory
MemRead
MemWrite
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
ALUSrc
ALUOp
RegDst
RegWrite
Branch
PCSrc
MemtoReg
R1  Mem[R2+30]
PC
PC+4
[R2]
30
1

## Slide 14: Pipelined execution: Load (cycle 3 – EXE)
op
rs
rt
immediate
0
16
21
26
31
2
1
30
LW
LW R1, (30)R2 ;
6
ALU
result
zero?
result
Add
Shift
left 2
ALU
Control
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
Address
Write
Data
Read
Data
Data
Memory
MemRead
MemWrite
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
ALUSrc
ALUOp
RegDst
RegWrite
Branch
PCSrc
MemtoReg
R1  Mem[R2+30]
PC
[R2]+30
1

## Slide 15: Pipelined execution: Load (cycle 4 – MEM)
op
rs
rt
immediate
0
16
21
26
31
2
1
30
LW
LW R1, (30)R2 ;
6
ALU
result
zero?
result
Add
Shift
left 2
ALU
Control
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
Address
Write
Data
Read
Data
Data
Memory
MemRead
MemWrite
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
ALUSrc
ALUOp
RegDst
RegWrite
Branch
PCSrc
MemtoReg
R1  Mem[R2+30]
PC
DATA
1

## Slide 16: Pipelined execution: Load (cycle 5 – WB)
op
rs
rt
immediate
0
16
21
26
31
2
1
30
LW
LW R1, (30)R2 ;
6
ALU
result
zero?
result
Add
Shift
left 2
ALU
Control
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
Address
Write
Data
Read
Data
Data
Memory
MemRead
MemWrite
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
ALUSrc
ALUOp
RegDst
RegWrite
Branch
PCSrc
MemtoReg
R1  Mem[R2+30]
PC
DATA
1

## Slide 17: Pipelined execution: cycle 1
6
ALU
result
zero?
result
Add
Shift
left 2
ALU
Control
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
Address
Write
Data
Read
Data
Data
Memory
MemRead
MemWrite
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
ALUSrc
ALUOp
RegDst
RegWrite
Branch
PCSrc
MemtoReg
lw
4
0 lw R10,9(R1)
4 sub R11,R2,R3
8 and R12,R4,R5 12 or R13,R6,R7
PC
0

## Slide 18: Pipelined execution: cycle 2
6
ALU
result
zero?
result
Add
Shift
left 2
ALU
Control
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
Address
Write
Data
Read
Data
Data
Memory
MemRead
MemWrite
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
ALUSrc
ALUOp
RegDst
RegWrite
Branch
PCSrc
MemtoReg
sub
8
0 lw R10,9(R1)
4 sub R11,R2,R3
8 and R12,R4,R5 12 or R13,R6,R7
PC
4
4
R10
[R1]
9

## Slide 19: Pipelined execution: cycle 3
6
ALU
result
zero?
result
Add
Shift
left 2
ALU
Control
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
Address
Write
Data
Read
Data
Data
Memory
MemRead
MemWrite
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
ALUSrc
ALUOp
RegDst
RegWrite
Branch
PCSrc
MemtoReg
and
12
0 lw R10,9(R1)
4 sub R11,R2,R3
8 and R12,R4,R5 12 or R13,R6,R7
PC
8
8
R11
[R2]
[R1]+9
R10
[R3]

## Slide 20: Pipelined execution: cycle 4
6
ALU
result
zero?
result
Add
Shift
left 2
ALU
Control
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[15-0]
[20-16]
[15-11]
Sign
extend
16
32
ID/EX
EX/MEM
MEM/WB
Instruction
Address
Write
Data
Read
Data
Data
Memory
MemRead
MemWrite
4
Instruction
Memory
Address
Add
IF/ID
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
ALUSrc
ALUOp
RegDst
RegWrite
Branch
PCSrc
MemtoReg
or
16
0 lw R10,9(R1)
4 sub R11,R2,R3
8 and R12,R4,R5 12 or R13,R6,R7
PC
12
12
R12
[R4]
[R3]-[R2]
R11
[R5]
Mem([R1]+9)
R10

## Slide 21: Pipeline hazards: Data Hazard

## Slide 22: Data Hazard
Problem with starting next instruction before the previous ones are finished
  Dependencies that “go backward in time” are data hazards
sub R2, R1, R3
and R12,R2, R5
or R13,R6, R2
add R14,R2, R2
sw R15,100(R2)
Program
execution
order
1
2
3
4
5
6
Time (clock cycles)
7
8
9
10
Value of R2
10
10
10
-20
-20
-20
-20
10 / -20
I
M
R
e
g
I
M
R
e
g
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
I
M
D
M
R
e
g
D
M
R
e
g
R
e
g
R
e
g
R
e
g
D
M

## Slide 23: Data Hazard: HW Solution 1 - Add Stalls
Have the hardware detect hazard and add stalls if needed
Problem: this also slows us down!
I
M
bubble
bubble
bubble
bubble
I
M
bubble
bubble
bubble
bubble
I
M
bubble
bubble
bubble
bubble
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
R
e
g
I
M
R
e
g
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
R
e
g
R
e
g
D
M
sub R2, R1, R3
stall
stall
stall
and R12,R2, R5
or R13,R6, R2
add R14,R2, R2
sw R15,100(R2)
Program
execution
order
1
2
3
4
5
6
Time (clock cycles)
7
8
9
10
Value of R2
10
10
10
-20
-20
-20
-20
10 / -20

## Slide 24: Data Hazard: HW Solution 2 - Forwarding
Don’t wait for results to be written into the register file, use it as soon as it is calculated
sub R2, R1, R3
and R12,R2, R5
or R13,R6, R2
add R14,R2, R2
sw R15,100(R2)
Program
execution
order
1
2
3
4
5
6
Time (clock cycles)
7
8
9
10
Value of R2
10
10
10
-20
-20
-20
-20
10 / -20
I
M
R
e
g
I
M
R
e
g
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
I
M
D
M
R
e
g
D
M
R
e
g
R
e
g
R
e
g
R
e
g
D
M

## Slide 25: Forwarding Hardware
Control
EX
M
WB
Forwarding
Unit
1
m
u
x
0
0
m
u
x
1
0
m
u
x
B
1
2
0
m
u
x
A
1
2
Data
Memory
ALU
Register
File
Instruction
Memory
PC
ID/EX
EX/MEM
MEM/WB
IF/ID
Instruction
IF/ID.Rs
IF/ID.Rt
IF/ID.Rt
IF/ID.Rd
Rs
Rt
Rt
Rd
WB
M
WB
EX/MEM.Rd
MEM/WB.Rd
EX/MEM.RegWrite
MEM/WB.RegWrite

## Slide 26: Forwarding Control
EXE Hazard:
  if (EX/MEM.RegWrite && (EX/MEM.WriteReg == ID/EX.ReadReg1)) ALUSelA = 1
  if (EX/MEM.RegWrite && (EX/MEM.WriteReg == ID/EX.ReadReg2)) ALUSelB = 1
MEM Hazard:
  if (MEM/WB.RegWrite && ALUSelA != 1 && (MEM/WB.WriteReg == ID/EX.ReadReg1))
  ALUSelA = 2
  if (MEM/WB.RegWrite && ALUSelB != 1 && (MEM/WB.WriteReg == ID/EX.ReadReg2))
  ALUSelB = 2

## Slide 27: Forwarding Hardware Example: bypassing from EXE to Src1 and from WB to Src2
lw R11, 9(R1)
Control
EX
M
WB
Forwarding
Unit
1
m
u
x
0
0
m
u
x
1
0
m
u
x
1
2
0
m
u
x
1
2
Data
Memory
Register
File
Instruction
Memory
PC
ID/EX
EX/MEM
MEM/WB
IF/ID
Instruction
IF/ID.Rs
IF/ID.Rt
IF/ID.Rt
IF/ID.Rd
Rs
Rt
Rt
Rd
WB
M
WB
EX/MEM.Rd
MEM/WB.Rd
10
ALU
lw
[R10]
Data from
memory
address
[R1]+9
sub
[R11]
12
and
11
[R2]-[R3]
11
10
sub R10, R2, R3
and R12, R10, R11

## Slide 28: Can't always forward
A hazard detection unit has to “stall” the instruction following the load
Load word can still causes a hazard:
  an instruction follows a load instruction and reads the same register that is written by the load.
I
M
R
e
g
R
e
g
I
M
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
I
M
D
M
R
e
g
D
M
R
e
g
R
e
g
R
e
g
D
M
Program
execution
order
lw R2, 30(R1)
and R12,R2, R5
or R13,R6, R2
add R14,R2, R2
sw R15,100(R2)
1
2
3
4
5
6
Time (clock cycles)
7
8
9
R
e
g
Need it here!

## Slide 29: Stalling
De-assert the write enable to ID/EXE
  The dependent instruction (and) stays another cycle in IF/EXE
De-assert the write enable to the IF/ID latch, and to the PC
  Freeze pipeline stages preceding the stalled instruction
Issue a NOP into the EXE/MEM latch (instead of the stalled inst.)
Allow the stalling instruction (lw) to move on
R
e
g
I
M
R
e
g
R
e
g
I
M
D
M
I
M
R
e
g
D
M
R
e
g
I
M
I
M
D
M
R
e
g
I
M
D
M
R
e
g
D
M
R
e
g
R
e
g
R
e
g
R
e
g
Program
execution
order
lw R2, 30(R1)
and R12,R2, R5
or R13,R6, R2
add R14,R2, R2
sw R15,100(R2)
1
2
3
4
5
6
Time (clock cycles)
7
8
9
bubble

## Slide 30: Hazard Detection (Stall) Logic
if (ID/EX.RegWrite && ID/EX.opcode == lw && (ID/EX.WriteReg == IF/ID.ReadReg1 || ID/EX.WriteReg == IF/ID.ReadReg2)
stall = 1

## Slide 31: Forwarding + Hazard Detection Unit
Control
EX
M
WB
Forwarding
Unit
1
m
u
x
0
0
m
u
x
1
0
m
u
x
1
2
0
m
u
x
1
2
Data
Memory
ALU
Register
File
Instruction
Memory
PC
ID/EX
EX/MEM
MEM/WB
IF/ID
Instruction
IF/ID.Rs
IF/ID.Rt
IF/ID.Rt
IF/ID.Rd
Rs
Rt
Rt
Rd
WB
M
WB
EX/MEM.Rd
MEM/WB.Rd
Hazard
Detection
Unit
0
ID/EX.MemRead
PC Write
0
m
u
x
1
IF/ID Write
ID/EX.Rt

## Slide 32: Software Scheduling to Avoid Load Hazards
Example: code for (assume all variables are in memory):
a = b + c;
d = e – f;
Slow code
LW Rb,b
LW Rc,c
Stall ADD Ra,Rb,Rc
SW a,Ra
LW Re,e
LW Rf,f
Stall SUB Rd,Re,Rf
SW d,Rd
Instruction order can be changed as long as the correctness is kept
LW Rb,b
LW Rc,c
LW Re,e
ADD Ra,Rb,Rc
LW Rf,f
SW a,Ra
SUB Rd,Re,Rf
SW d,Rd

## Slide 33: Pipeline modeling

## Slide 34: Single-Cycle Implementation modeling
void MIPS::run(const string& tr) {
// ... load trace
this->PC = startPC;
for (uint i = 0; i < instr_to_run; ++i) {
uint32 bytes = fetch(); // fetch() { return mem->read(PC); }
FuncInstr instr(bytes);
read_src(instr); // read_src() { instr->v_src1 = rf->read(instr->rs); …}
instr->execute(); // execute_add() { v_dst = v_src1 + v_src2; }
ld_st(instr);
wb(instr); // wb() { rf->write(instr->rd, instr->v_dst); }
PC = update_pc(instr);
}
F
D
E
M
W
class MIPS {
// storages of internal state
RF* rf;
uint32 PC;
Memory* mem;
void ld_st(FuncInstr& inst);
void wb(const FuncInstr& inst);
public:
MIPS();
void run(const string&, uint instr_to_run);
};

## Slide 35: Performance modeling
In single-cycled MIPS every instruction is executed in 1 cycle
To get pipelined MIPS performance, we have to model timing of each pipeline stage of instruction due to stalls
In HW, pipeline stages are divided by latches that are updated every cycle.
Modeling of latch is possible, but its interface is complicated The more convenient solution is called ports

## Slide 36: Ports
From interface port of view, one port consists of two parts, implemented in classes ReadPort and WritePort
class Module1 {
WritePort<uint>* wp;
Module1() {
wp = new WritePort<uint>(“DATA_PORT”);
wp->set_bandwidth(1);
}
};
class Module2 {
ReadPort<uint>* rp;
Module2() {
rp = new ReadPort<uint>(“DATA_PORT”);
rp->set_latency(5);
}
};
Ports are connected by equal string key
Module1::do_action(uint64 cycle) {
// …
wp->write(data, cycle);
}
// this method must be run every cycle!
Module2::clock(uint64 cycle)
uint data;
while (rp->is_ready(cycle)) {
// …
}
}
Imagine that here we following functions:
wp->write(8, 0);
wp->write(9, 2);
Let’s look how it will be executed here:
rp->is_ready(0); // data is trash, returns false
rp->is_ready(1); // data is trash, returns false
rp->is_ready(2); // data is trash, returns false
rp->is_ready(3); // data is trash, returns false
rp->is_ready(4); // data is trash, returns false
rp->is_ready(5); // data is 8, returns true!
rp->is_ready(6); // data is trash, returns false
rp->is_ready(7); // data is 9, returns true!

## Slide 37: Example: decoder
Decoder::clock(uint64 cyc) {
if (rp_fetch_to_decoder->is_ready(cyc)) {
this->dec_bytes = rp_fetch_to_decoder->read(cyc);
this->instr = FuncInstr(dec_bytes);
}
read_src(this->instr);
if (this->instr.srcs_ready){
wp_decoder_to_execute->write(instr, cyc);
wp_decoder_to_fetch->write(false, cyc);
}
else {
wp_decoder_to_fetch->write(true, cyc);
}
}
Executor::clock(uint64 cyc) {
while (rp_decoder_to_execute->read(cyc)) {
FuncInstr instr = rp_decoder_to_execute->read(cyc);
instr->execute();
// … to ldst and writeback
}
}
MIPS::clock(uint64 cyc) {
this->decoder->clock(cyc);
this->executor->clock(cyc);
}

## Slide 38: Extra reading
Asim: A Performance Model Framework http://www.ckluk.org/ck/papers/asim_ieeecomputer.pdf
Manual on MIPT-MIPS Ports https://github.com/MIPT-ILab/mipt-mips/wiki/Communication-between-modules-through-ports

## Slide 39: Thank You