## Slide 1: Caches
Pavel Kryukov Kirill Korolev
15 February 2019 22 February 2019

## Slide 2: Agenda
Memory Wall
Spatial and temporal locality
Hardware implementations
Performance metrics
Software optimizations
Hardware optimizations
  Prefetching
  Replacement
Write handling
Multi-level cache organization
Modeling in simulator

## Slide 3: Memory Is Slow
CPU
DRAM
60% per year
(Doubles every 1.5 year)
9% per year
(Doubles every 10 year)
Performance gap

## Slide 4: Why is memory slow?
A1: Memory uses DRAM technology, while registers are SRAM
  DRAM is slower, but cheaper
  This is not the answer: may we use SRAM for memory?
A2: Memory transistors are smaller, therefore they are slower
  Again: may we use big transistors for memory?
DRAM cell
SRAM cell

## Slide 5: Correct answer is: density/latency balance
Large memory arrays have large area, so wires have to be long
Large memory cannot be fast. Fast memory cannot be large.

## Slide 6: Refresher: Pipeline limitations
Max speed of the pipeline is one instruction per clock
It is rare achievable in in-order processors due to dependencies among instructions and long latency operations
 |  |  | F | D | E | M | W |  | 
 |  |  |  | F | D | E | M | W | 
 |  |  |  |  | F | D | E | M | W
F | D | E | M | W |  |  |  |  | 
 | F | D | E | M | W |  |  |  | 
 |  | F | D | E | M | W |  |  | 
F | Stall |  | 
D | E | M | W |  | 
F | D | E | M | W | 
 | F | D | E | M | W
M | W
Load from the memory

## Slide 7: Memory Hierarchy
Main memory is large, but too slow
Small memory is fast, but cannot hold all required data
Solution: take the best of both and combine
Memory hierarchy provides visibility that memory is usually fast
L1
L2
L3
Cache
CPU
Main Memory
smallest, but fastest
slowest, but largest

## Slide 8: Real life example: Logistics
Your shop
Factory
Shop store
Storehouse
Large storehouse
The delay is decreased, but the cost is increased

## Slide 9: Real life example: bookshelf
A-B | C-D | E-F | G-H | I-J | … | … | … | … | … | Y-Z
The first letter in the name of the author
Places for books
Your table
fast
slow
Your bookshelf
City library

## Slide 10: Why Does It Work?
Temporal Locality (Locality in Time):
  If an item is accessed, it will tend to be accessed again soon
  Example: code and variables in loops
→ Keep recently accessed data closer to the processor
Spatial Locality (Locality in Space):
  If an item is accessed, nearby items tend to be accessed soon
  Example: scanning an array
→ Move contiguous blocks closer to the processor
Locality + smaller HW is faster memory → hierarchy

## Slide 11: Localities are usually contradicting
Read of a large data array (data size >> cache size) has spatial locality, but no temporal locality
Read of a single variable has temporal locality, but no spatial locality
  for (size_t i = 0; i < N; ++i)
  sum += a[i];
  for (size_t i = 0; i < N; ++i)
  sum += i + *a;

## Slide 12: Cache implementation

## Slide 13: Cache: Main Idea
The cache holds a small part of the entire memory
  Need to map parts of the memory into the cache
Main memory is virtually partitioned into lines
  Typical block size is 32 to 64 bytes
  Blocks are aligned
The cache holds data by lines
  Only a subset of the blocks is mapped to the cache at a given time
Address of lines is used as a key
Memory
Cache
#line
#line
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
2 | 
91 | 
4 | 
5 | 

## Slide 14: Cache Lookup
Case 1: Cache Hit
  The requested line is in the cache
  The cache returns the requested line (fast)
Case 2: Cache Miss
2 | 
91 | 
5 | 
Memory
Cache
line#
line#
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
4?
4
hit
CPU

## Slide 15: Cache Lookup
Case 1: Cache Hit
  The requested line is in the cache
  The cache returns the requested line (fast)
Case 2: Cache Miss
  The requested line is not in the cache
  Need to fetch it from the main memory (slow) and fill the cache
  May need to evict another line from the cache to free space for the new one
91 | 
5 | 
Memory
Cache
line#
line#
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
93?
4
miss
2
93
93?
CPU

## Slide 16: Fully Associative Cache
Line may be mapped to any cache entry
  Lookup line in all entries
Address is partitioned to
  Offset within a line (byte#)
  Line # (so-called tag)
Each cache entry has a tag
  All tags are compared to the line# in parallel
  If one of the tags matches the line#, we have a hit
data
63
0
…
hit/miss
=
=
=
…
…
Tag
Array
Data
Array
64 | 5 | 0
Tag = line# | Offset | 
Address
0 | 
1 | 
… | 
511 | 

## Slide 17: Direct Mapped Cache
Line is mapped to the fixed entry only
  Lookup line in one entry
Address is partitioned to
  Offset within a line (byte #)
  Set (fixed cache entry #)
  Tag (works as a key)
Conflicts are possible
  If several lines are mapped to the same entry, only one can reside in the cache
data
0 |  |  | 
1 |  |  | 
… |  |  | 
511 |  |  | 
63
0
Tag Array
Data
Array
Address
64 | 14 |  | 5 | 0
Tag | Set |  | Offset | 
…
hit/miss
=
set#

## Slide 18: Memory Layout: Direct Mapped Cache
Memory is virtually partitioned
  into lines
    line size = 2 ^ offset_size
  lines grouped into slices
    # of lines in slices = 2 ^ set_size
    slice size = # of lines in slice * line_size = cache size
  slice # = tag value
  line # inside a slice = set value
Disadvantage is line evictions due to set conflicts
tag#
…
cache size
cache size
cache size
cache size
Memory Space
set#
set#
set#
set#
Mapped to the same set
 | Offset
 | Set | Offset
Tag | Set | Offset
0
64

## Slide 19: 2-Way Set Associative Cache
Conflicts are harmful → multi-ways cache is a solution
Each set holds two entries (way 0 and way 1)
  Each line can be mapped into one of two entries in the appropriate set
Address
64 | 13 |  | 5 | 0
Tag | Set |  | Offset | 
0 |  |  | 
1 |  |  | 
… |  |  | 
255 |  |  | 
63
0
Tag Array
Data Array
way #1
set#
0 |  |  | 
1 |  |  | 
… |  |  | 
255 |  |  | 
63
0
Tag Array
Data Array
way #0
set#

## Slide 20: 2-Way Set Associative Cache
Address
64 | 13 |  | 5 | 0
Tag | Set |  | Offset | 
0 | 
1 | 
… | 
255 | 
63
0
way #0
way #0
set#
hit/miss
=
0 | 
1 | 
… | 
255 | 
set#
way #1
=
63
0
way #1
Tag Array
Data Array
MUX
data

## Slide 21: Memory Layout: Multi-Way Cache
Memory is virtually partitioned almost the same as in direct map cache
  The only difference is slice size
    slice size = cache size / # of ways
Compared to direct map cache
  Decrease slice size → increase # of slices → increase # of lines mapped to the same set
  But in each set we can have multiple lines (= # of ways) at a given time
Example: 32KB, 8 ways, 64B line
  way size = 32KB / 8 = 4KB
  # of sets = 4KB / 64B = 64
…
way size
Memory Space
set#
Mapped to the same set
64 | 11 |  | 5 | 0
Tag | Set |  | Offset | 
address

## Slide 22: Memory Layout: Multi-Way Cache
Slice is Nx smaller
For fully-associative cache N is equal to cache size in lines
For direct mapped cache N == 1
Address partitioning formulas:
63 | Y |  | X | 0
Tag | Set |  | Offset | 
X = log(block_size)
Y = log(cache_size / N)
…
slice
set #
Mapped to N cache lines

## Slide 23: Performance metrics

## Slide 24: Cache Performance
Terms:
  Miss Rate = Misses / total CPU request
  Hit Rate = Hits / total CPU request = 1 – Miss Rate
Cache goal is decreasing average memory access time (AMAT)
  AMAT = Hit Rate * Hit Time + Miss Rate * Miss Penalty
  AMAT ≈ Hit Time + Miss Rate * Miss Penalty
Example:
  HitRate ≈ 0.9, HitTime ≈ 4 clk, MissRate ≈ 0.1, MissPenalty ≈ 200 clk, then…
  AMAT = 0.9 * 4 + 0.1 * 200 = 23.6 clk
  AMAT w/o cache = 200 clk
  About 10x improve!

## Slide 25: Motivation for multi-level caches
L1 cache: AMAT ≈ HitTimeL1 + MissRateL1 * MissPenaltyL1
L2 reduces L1 miss penalty – saves access to memory
Now, on L1 miss we access L2, but not memory
  MissPenaltyL1 ≈ HitTimeL2 + MissRateL2 * MissPenaltyL2
L2 Cache is larger (better HitRate), but has higher latency
Example:

## Slide 26: Three Types of Cache Misses (3-C)
Compulsory misses
  Those that occurs even in a infinite cache
  First access to data
  So-called cold misses
Capacity misses
  Those that occurs in an fully associative cache
  Workset is larger than the cache size
Conflict misses
  Difference between fully associate and direct mapped cache
  The size of the cache is enough, but the problem is in line mapping to sets
Compulsory
Conflict
Capacity
Miss Rate = F(Cache Capacity, Associativity)

## Slide 27: Software Optimizations

## Slide 28: Loop Fusion
Combine loops that have same looping and work with the same memory
  Assume each element is 8 bytes, 32KB cache, 64 B/line
  for (i = 0; i < 10240; i++)
  a[i] = 1 / a[i];
  …
  for (i = 0; i < 10240; i++)
  sum = sum + a[i];
  Fuse the loops
  for (i = 0; i < 10240; i++) {
  a[i] = 1 / a[i];
  sum = sum + a[i];
  }
Improves temporal locality

## Slide 29: Loop Interchange
Change loops nesting to access data in order stored in memory
  Two dimensional array in memory:
x[0][0] x[0][1] … x[0][99] x[1][0] x[1][1] …
  Before:
  for (j = 0; j < 100; j++)
  for (i = 0; i < 5000; i++)
  x[i][j] = 2 * x[i][j];
  Improves spatial locality
  Sequential accesses instead of striding through memory every 100 words
  for (j = 0; j < 100; j++)
  After:
  for (i = 0; i < 5000; i++)
x[i][j] = 2 * x[i][j];
  for (i = 0; i < 5000; i++)
  for (j = 0; j < 100; j++)
  x[i][j] = 2 * x[i][j];

## Slide 30: “Stop using linked lists”
Linked lists have no spatial locality
  → cache handles them worse than arrays
  → O(N) operation with array is much faster than O(N) operation with list
Example: random insert after linear search
https://kjellkod.wordpress.com/2012/02/25/why-you-should-never-ever-ever-use-linked-list-in-your-code-again

## Slide 31: AoS vs SoA
Array of structures (AoS)
struct map {
int val;
int key;
// ...
} merged_array[SIZE];
Locality if value and key are used together
Worse utilization otherwise
Structure of arrays (SoA)
struct map {
int val[SIZE];
int key[SIZE];
// ...
} merged_struct;
Locality if value and key are used independently
Possible inter-set conflicts between values

## Slide 32: Data alignment
Example: cache line size is 64 bytes, we load 4 bytes by address 0x3c
  How many cache lines has to be looked up?
  What if the first is hit and the second is miss?
Preferable solution: align memory access in a cache line
  Required by many ISA, e.g. MIPS, RISC-V, x86 vector extensions
  Basic sizeof(long double) alignment guaranteed by C
Alternative solution: add HW to make two accesses
  Handles legacy cases and has worse performance (Amhdal’s law)

## Slide 33: Agenda, part 2
Memory Wall
Spatial and temporal locality
Hardware implementations
Performance metrics
Software optimizations
Hardware optimizations
  Prefetching
  Replacement
Write handling
Multi-level cache organization
Modeling in simulator

## Slide 34: Refresher
Main memory is large, but slow
Solution: memory hierarchy with caches
  utilizes temporal and spatial locality of workloads
  provides visibility that memory is usually fast
Bad scenario: cache misses
  Compulsory
  Capacity
  Conflict
L1
L2
L3
Cache
CPU
Main Memory
smallest, but fastest
slowest, but largest

## Slide 35: Prefetching

## Slide 36: Prefetching: main idea
Prefetching – predict future memory accesses
  A useful prefetch eliminates a potential cache miss
2 types of prefetching:
  Software Prefetching: special prefetching instructions
  Hardware Prefetching
Code prefetching is performed by a branch predictor
Prefetch Limitations
  Prefetching relies on extra memory bandwidth
  Too aggressive/inaccurate prefetching slows down demand fetches

## Slide 37: Quality metrics
Accuracy
  Portion of prefetched lines which eventually become demand-hits
Coverage
  Portion of cache misses removed by prefetching
Timeliness
  Reduction of cache miss time
For L1 cache prefetch schemes with high accuracy are used
Bigger caches usually leverage schemes with higher coverage

## Slide 38: Next sequential
On a cache miss, prefetch sequential cache line (± 64 bytes)
Prefetch metrics:
  Moderate accuracy
  Low coverage
  Lack of timeliness (prefetch performed too late)
Simple HW
Works well for instructions prefetch
“Fallback" if more complex methods not available
  lw $t0, 0x0($t1)
prefetch 0x40($t1)

## Slide 39: Stride detection
HW detects the repetitive step of a load and prefetch data in advance
Prefetch metrics:
  High accuracy (for long loops)
  Low coverage
  Highly timeliness
Issues with unrolled loops
  Initially single load operation occupies multiple entries in detector
  0x00402f0: lw $t0, 0x20($t1)
  0x00402f4: add $t2, $t2, $t0
  0x00402f8: addi $t1, $t1, 0x100
  0x00402fc: beq $t1, $t3, -4
IP | Stride | Last address
0x00402f0 | 0x100 | 0x00f4180
prefetch 0x00f4280
prefetch 0x00f4380
...
Detector

## Slide 40: Stream detection (1)
HW detects stream with the repetitive step
  Similar to the previous technique, but without reference to IP
Example:
0xba20200
0x3cf1140 0xba203с0
0x3cf1100
0x3cf10c0
0x3cf1080
0xba20740
0xba20900
...
prefetch 0xba20ac0
prefetch 0x3cf1040
...
Base address | Stride | Last address
0xba20200 | +0x1c0 | 0xba20900
0x3cf1140 | −0x40 | 0x3cf1080
0xba20200
0x3cf1140 0xba203с0
0x3cf1100
0x3cf10c0
0x3cf1080
0xba20740
0xba20900
...

## Slide 41: Stream detection (2)
Stream detection without repetitive step
  load pattern not found, only direction – load everything following this direction
Prefetch metrics:
  Low accuracy
  High coverage
  Highly timeliness
0xba20200 0xba20340
0xba203a0
0xba204с0
0xba20520
...
prefetch 0xba20560
prefetch 0xba205a0
...
Base address | Stride | Last address
0xba20200 | +???? | 

## Slide 42: Replacement

## Slide 43: Cache Line Replacement
When miss occurs need to free space in a cache for a new line
Direct mapped cache
  A new line is mapped to a single entry → evict old line from the entry
N-way set associative cache
  Choose a victim from all ways in the appropriate set, but how?
FIFO (First In First Out) replacement
  Easy to implement in HW, but can violate temporal locality
LRU (Least Recently Used) replacement
  Evict the most unused line (was not accessed longer than other)
  Good temporal locality, but complex HW → use simplified pseudo-LRU

## Slide 44: Pseudo-LRU
Pseudo-LRU is a good approximation of LRU with a binary tree
Each node stores information about which of the descendants was recently used
L
R
L
A
B
C
D
R
L
L
A
B
C
D
Request «B»
L
R
R
A
B
E
D
R
R
L
A
B
C
D
Request «A»
Request «E»

## Slide 45: Counterexample
Sometimes there is no temporal locality
  Example: read of large data array (data size >> cache size)
In case of LRU the second loop will always ‘miss’
If data eviction follows MRU policy (most-recently used) the second loop will start with ‘hit’
  for (size_t i = 0; i < N; ++i)
  sum += a[i];
  double average = sum / N; for (size_t i = 0; i < N; ++i)
  a[i] -= average;

## Slide 46: Write handling

## Slide 47: Cache write policies
Memory writes (store instructions) also need to update a cache
WriteThrough: always update both memory and cache
  + Coherence: cache and memory are always in the same state
  - Higher utilization of memory bandwidth
WriteBack: update only cache, update memory at line eviction
  + Low store latency and memory bandwidth
  - Risk of data loss, requires snoops – coherency checks

## Slide 48: Multi-level cache organization

## Slide 49: Motivation for multi-level caches
Only L1 cache: a large miss penalty due to memory access
With L2 cache: L1 miss penalty is reduced
  Now, on L1 miss we access L2, not memory
L2 Cache is larger (lower MissRate), but has higher latency
Example:
L2
<T> ≈ T_L1hit + MissRateL1 * T_mem
<T> ≈ T_L1hit + MissRateL1 * (T_L2hit + MissRateL2 * T_mem)
<T> ≈ 3 + 0.08 * 200 = 19 clk
<T> ≈ 3 + 0.08 * (6 + 0.03 * 200) = 3.96 clk
x5 !
L1
CPU
Main Memory

## Slide 50: Multi-level inclusion policies
1. Inclusive
2. Exclusive
3. Non-Inclusive/Non-Exclusive (NINE)
L2
L1
L2
L1
modified only
modified only
M/NM
modified only
+ low bandwidth
- lines duplications
+ effective cache usage
- higher bandwidth
L2
L1
combination of 2 policies
M/NM
modified only