## Slide 1: OOO – part 2
Oleg Ladin
22.03.2021

## Slide 2: Refresher: Parallelism and Superscalar
Paralleling is a major performance boost in modern architectures
Paralleling uses parallelism of 2 types:
  ILP - independent instructions of a single process
  TLP - independent multiple processes – threads (in next lectures)
Superscalar extracts ILP
  A wide pipeline processes >1 instruction per cycle
  Alternatives – VLIW, vectorization (e. g. SIMD)
Notes: Why in-order Superscalar is still not good enough?

## Slide 3: Refresher: OOO execution
In-order Superscalar is limited by dependency stalls
Solution: execute independent instructions out of program order – Out-Of-Order execution
  Put all instructions in program order into the Reorder Buffer - ROB
  Check register dependencies (both source and destination)
  Execute independent instructions
  Keep a separate set of registers, updating it in-order – architectural state
So, a large ROB is good?
Notes: Why do we need the arch state?
How big should be the OOO window?

## Slide 4: Limitation #1: Branches
Fetch
Retire
Branch with unknown condition
All subsequent instructions are fetch according to prediction
…
Speculatively fetched instructions can be executed too
Verify the branch prediction
If prediction was wrong, all the subsequent instructions are deleted
deleted
How to fill a large window with instructions, if there are branches?
Are mispredictions really harmful?
  In average, each 5th instruction is a branch
  Assume accuracy of prediction is 90% (looks high, isn’t it?)
  The probability that 100th instruction in the window will not be removed is:
  (90%)^20 = 12%
Accuracy of branch prediction is very important for Out‑Of‑Order Execution
→ Using branch prediction!
(e.g., (99%)^20 = 82%)

## Slide 5: Limitation #2: Exceptions
In pipelined machine exceptions handling is complicated:
  Speculative code
  Simultaneous exceptions on different pipe stages
  Cancellation of consequent code
The solution was to postpone handling until writeback
  In OOO, we have retirement instead of writeback

## Slide 6: Limitation #2: Exceptions
At execution instruction that takes a fault/exception is marked
Instructions older than the marked instruction are retired
When the marked instruction retires – handle the fault
  Flush the ROB
  Initiate the handling code according to the type
  Re-fetch the faulting instruction and the subsequent instructions
Fetch
Retire
Instruction that caused exception
…
deleted

## Slide 7: Interrupts
If an interrupt occurs, let the oldest instruction retire, flush everything younger and proceed to handling:
F
D
A
E
F
D
A
F
D
A
E
F
D
A
E
R
F
D
A
E
R
F
D
A
F
D
A
F
D
A

## Slide 8: Limitation #3: False Dependencies
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r5  r5 + 1
(4) r6  r6 – r3
(5) r4  load [r5 + r6]
(6) r7  r8 * r4
Out-of-order execution
Example:
1
3
4
2
5
6
r1
r5
r6
r4
r8
Data Flow Graph
4
3
6
5
1
2
r1
r1
r1
False Dependencies:
Write-After-Write: (1) → (3)
Write-After-Read: (2) → (3)
Significantly decrease performance

## Slide 9: Eliminating False Dependencies
Register name is similar to variable name in a program
  It is just a label to identify dependency among operations
Difference: number of register names is limited by ISA
  It is one of the main reason of false dependencies
HW can contain more registers in the speculative state (i.e. more names) than ISA and perform dynamic register renaming
  Number of registers in arch state is not changed (= ISA)
Requirements
  Producer and all its consumers are renamed to the same speculative register
  Producer writes to the original arch register at retirement
(2) …  ar3 + …
(1) ar3  …
(4) …  ar3 + …
(3) ar3  …
sr10
sr10
sr11
sr11

## Slide 10: Register Renaming Algorithm
Redo register allocation that was done by compiler
Eliminate all false dependencies
(1) r1  r4 / r7
(2) r8  r1 + r2
(3) r1  r5 + 1
(4) r6  r6 – r3
(5) r4  load [ r1 + r6 ]
(6) r7  r8 * r4
Example:
Renaming
pr10 ≡ r1
pr11 ≡ r8
pr12 ≡ r1
pr13 ≡ r6
pr14 ≡ r4
pr15 ≡ r7
 | r0 | r1 | r2 | r3 | r4 | r5 | r6 | r7 | r8
pr10
pr11
pr15
pr14
pr12
pr13
pr10
pr10
pr11
pr11
pr12
pr12
pr13
pr13
pr14
pr14
Register Aliases Table (RAT)
pr15

## Slide 11: RAT Restore
Each ROB entry saves previous register alias (history)
On flush, ROB restores history
(1) r1  r4 / r7
(2) r8  r1 + r2
r1  r5 + 1
jump
(5) r6  r6 – r3
(6) r4  load [ r1 + r6 ]
(7) r7  r8 * r4
Example:
Renaming
pr10 ≡ r1
pr11 ≡ r8
pr12 ≡ r1
pr13 ≡ r6
pr14 ≡ r4
pr15 ≡ r7
 | r0 | r1 | r2 | r3 | r4 | r5 | r6 | r7 | r8
 |  | pr7 |  |  | pr21 |  | pr20 | pr3 | pr8
pr10
pr11
pr15
pr14
pr12
pr13
pr10
pr10
pr11
pr11
pr12
pr12
pr13
pr13
pr14
pr14
Register Aliases Table (RAT)
pr15
r1 was pr7
r8 was pr8
r1 was pr10
r6 was pr20
r4 was pr21
r7 was pr3
History

## Slide 12: Why Is ROB Complex?
The two complex searches though all ROB entries
  At allocation (once per each instruction): to identify producers of the instruction sources
  At scheduling (every cycle): to identify ready instructions and send them to execution
The larger ROB the longer search and large HW structures
  Prevents from doing ROB really large -> loose potential performance
ROB
Out-of-order execution
PRF
EXE
Scheduler
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Memory
Write data
from decoder

## Slide 13: Scheduler Queue
It is enough to check only not completed instructions
  Their number is usually significantly less than ROB size (20-30%)
Decision:
  Create a smaller queue for not completed instructions only (scheduling queue or reservation stations)
ROB
Out-of-order execution
PRF
EXE
Scheduler
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Memory
Write data
from decoder

## Slide 14: Scheduler Queue
It is enough to check only not completed instructions
  Their number is usually significantly less than ROB size (20-30%)
Decision:
  Create a smaller queue for not completed instructions only (scheduling queue or reservation stations)
  All checks (allocation and scheduling) are performed on it
  Use ROB only for order reconstruction at retirement
Out-of-order execution
PRF
EXE
Scheduler
Memory
ROB
SQ
Allocation
Retirement
ARF
Check
Dependencies
Rename Registers
Write data
from decoder

## Slide 15: SQ Operation Example
 | Dst | Src 1 | Src 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
… |  |  | 
N |  |  | 
Ready?
Producers |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | … | N
Dependency Matrix
Free entries
(1) r1  …
(2) r2  …
(3) …  r1 + r2
1
5
3
r1
…
…
r2
…
…
r2
…
r1
1
1
Example:
At allocation of (3):
Search for Src1 producer
  Found in entry 1
    Mark dependency
Search for Src2 producer
  Found in entry 5
    Mark dependency
At least one is found -> not ready
false

## Slide 16: SQ Operation Example
 | Dst | Src 1 | Src 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
… |  |  | 
N |  |  | 
Ready?
Producers |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | … | N
Dependency Matrix
Free entries
(1) r1  …
(2) r2  …
(3) …  r1 + r2
r1
…
…
r2
…
…
r2
…
r1
1
1
Example:
At completion of (1,2):
Reset dependency to all consumers
For each entry check its readiness
false
true

## Slide 17: Thank You