## Slide 1: RISC-V ISA
Kirill Korolev
25 October 2021

## Slide 2: Step into Microarchitecture world…
2 next lectures will be
  More detailed overview of RISC-V ISA (today)
  The simplest uArch implementation of RISC-V ISA (next week)
The simulator overview along the way
  How to build/run/contribute to the GitHub project
You’ll get home tasks in the simulator along the way
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture (uArch)
Gates/Register-Transfer Level (RTL)
Circuits
Physics
1.
2.

## Slide 3: Refresher: ISA
Instruction Set Architecture (ISA) is a precise definition of computer:
    instructions
    registers and memory organization
    data formats
    interrupts and exceptions
It can be thought as an agreement between a programmer and an engineer

## Slide 4: RISC-V: overview
RISC-V is a modern RISC architecture
  Evolution of MIPS
Designed for customization:
  Modular
  Expandable through a variable instruction length
Open-source and actively evolved by community
  The first 6 RISC-V CPU created
  Supported by GCC and LLVM
RISC-V: The Free and Open RISC Instruction Set Architecture

## Slide 5: RISC-V: extensions
RISC-V is a modular ISA
  Use common naming convention for all modules
  A base integer ISA is required to be implemented
    40 instructions
  Other extensions – optional
RV
32
64
128
I = Integer
M = Integer Mul. & Div.
A
F = Floating single-precision
D = Floating double-precision
G = IMAFD = General
Q = Floating quad-precision
L
C = Compressed (16-bit ops)
B = Bit manipulation
J
T
P = Packed (SIMD instructions)
V = Vector instructions
N
RV32I
(BASIC)
A register size in bits
Extension

## Slide 6: RISC-V: “load-store” three-addresses design
RISC-V is a load-store or register-to-register ISA
  Only special instructions like load and store access the main memory
  All data manipulation (e. g. logic, arithmetic) occur between registers
RISC-V uses three-addresses instructions for data manipulation
  Each ALU instruction contains a destination and two sources
  For example, an addition instruction (a = b + c) has the form:
add a, b, c
operands
operation
destination
source 1
source 2

## Slide 7: RISC-V: Memory
Little-Endian
Byte-addressable address space
  where n – a register size ( for RV32I)
Addressing is circular
  Address calculation overflow is ignored

## Slide 8: RISC-V: registers
GPR = General Purpose Registers:
  32 32-bit integer registers x0-x31
  32 registers => 5-bit register addresses
  x0 hard-wired to 0
  F extension adds 32 floating-point registers f0-f31
CSR = Control and Status Registers
  pc = Program Counter – contains an address of the current instruction
  fsr = FP Status Register – FP rounding mode
  …
More registers = better?
  More registers → Larger decoders, multiplexers, etc. → larger circuits delays
  Instruction length is affected, as need more space to encode register numbers

## Slide 9: RISC-V: instructions
A RISC-V instruction is a bit “word” by default
  Fixed 32-bit length
  Encodes an operation & operands
Length can be variated with special bits
  Down to 16 bits (Compressed)
  Up to 192 bits
***********bbb11
****************
32-bit
**************aa
16-bit
************
**********011111
****************
48-bit
aa ≠ 11
bbb ≠ 111

## Slide 10: RV32I: instruction formats
4 core instruction formats: R, I, S, U
  +2 more variants with immediates: B & J
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
imm[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
imm[11:5] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | imm[4:0] |  |  |  |  | opcode |  |  |  |  | 1 | 1
i | imm[10:5] |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | imm[4:1] |  |  |  | i | opcode |  |  |  |  | 1 | 1
imm[31:12] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
i | imm[10:1] |  |  |  |  |  |  |  |  |  | i | imm[19:12] |  |  |  |  |  |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
R
I
S
U
B
J
source reg. 2
source reg. 1
destination reg.

## Slide 11: RV32I: arithmetic

## Slide 12: RV32I: reg-reg (R-type) arithmetic
OP rd, r1, r2
  Reads r1 and r2 registers, writes the result to rd register
All basic arithmetic operations:
  ADD, SUB, AND, OR, XOR
  SLT/SLTU (Set Less Than): 1 if rs1 < rs2 else 0
  SLL/SRL/SRA (Shift Left/Right Logical/Arithmetical)
Example: ADD x10, x10, x0
  x10 += 0
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1

## Slide 13: RV32I: reg-imm (I/U-type) arithmetic
I-type: OP rd, rs1, imm
  1 source register is replaced by a value from the instruction code – immediate
  ADDI, SLTI/SLTIU, ANDI/ORI/XORI, SLLI/SRLI/SRAI
U-type: OP rd, imm
  1 immediate operand only
  LUI = Load Upper Immediate – loads 20 upper bits, fills 12 lower bits with 0
  AUIPC = Add Upper Immediate to PC – don’t change pc register itself
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
imm[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
imm[31:12] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
I
U

## Slide 14: RV32I: NOP instruction
NOP = No Operation – instruction which does nothing
In MIPS: 32 zeroes
In RISC-V: 32 zeros is invalid
  ADDI x0, x0, 0 is used as a proxy

## Slide 15: RV32I: memory access

## Slide 16: RV32I: Load and Store
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
offset[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
offset[11:5] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | offset[4:0] |  |  |  |  | opcode |  |  |  |  | 1 | 1
I
S
The only instructions that may access the main memory:
  L[WHB] = Load form memory to a register (I-type): rd = memory[rs1 + offset]
    LB and LH do sign extension, LBU and LHU – zero extension
  S[WHB] = Store to memory from a register (S-type): memory[rs1 + offset] = rs2
    12-bit offset is split in 2 parts
Differs by a size of transferred data:
  W = Word = 32 bits
  H = Half Word = 16 bits
  B = Byte = 8 bits

## Slide 17: RV32I: control transfer

## Slide 18: RV32I: Unconditional jumps
2 instructions:
  JAL = Jump And Link (U-type): rd = pc + 4; target pc = pc + (offset << 1)
  JALR = Jump And Link Register (I-type): rd = pc + 4; target pc = rs1 + offset
Used for procedures calls
  rd contains a “return” address
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
offset[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
offset[31:12] |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
I
U

## Slide 19: RV32I: Conditional branches
Compares rs1 with rs2 and jumps to a target pc, if a condition is met
  target pc = pc + (offset << 1)
  Uses S-type encoding
4 different conditions => 4 instructions:
  BEQ = Branch, if equal (rs1 = rs2)
  BNE = Branch, if not equal (rs1 ≠ rs2)
  BLT[U] = Branch, if Less Than (rs1 < rs2)
  BGE[U] = Branch, if Greater or Equal (rs1 ≥ rs2)
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
offset[11:5] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | offset[4:0] |  |  |  |  | opcode |  |  |  |  | 1 | 1
S

## Slide 20: RISC-V Simulation
ALU class
  A collection of methods representing the target ISA operations
Decoder class
  takes raw 32 bit instruction
  provides instruction parameters (reg. ids, imm…) according to operation type
Instructions database
  Connection between the decoded opcode and ALU class method to call

## Slide 21: Source materials
RISC-V specifications and learning materials
Lectures:
  RISC-V-based: 6.375 (MIT) L9, CSE564 (OU) L7-8
  MIPS-based: CS378 (UW) L6-7

## Slide 22: Thank You