## Slide 1: MIPT-V 2021: Semester 2

## Slide 2: Semester 1 Refresher
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Hardware (HW)
Software (SW)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
HW/SW interface

## Slide 3: Caches: part 1
Kirill Korolev
7 February 2022

## Slide 4: Agenda
Memory Wall
Spatial and temporal locality
Hardware implementations
Performance metrics
Software optimizations
Hardware optimizations
  Prefetching
  Replacement
Write handling
Multi-level cache organization

## Slide 5: Memory Is Slow
CPU
DRAM
60% per year
(Doubles every 1.5 year)
9% per year
(Doubles every 10 year)
Performance gap

## Slide 6: Why is memory slow?
Memory uses DRAM technology, while registers are SRAM
  DRAM is slower, but cheaper
  This is not the answer: may we use SRAM for memory?
DRAM cell
SRAM cell

## Slide 7: Correct answer is density/latency balance
Large memory arrays have large area, so wires have to be long
Large memory cannot be fast. Fast memory cannot be large.

## Slide 8: Refresher: Pipeline limitations
Max speed of the pipeline is one instruction per clock
It is rare achievable in in-order processors due to dependencies among instructions and long latency operations
 |  |  | F | D | E | M | W |  | 
 |  |  |  | F | D | E | M | W | 
 |  |  |  |  | F | D | E | M | W
F | D | E | M | W |  |  |  |  | 
 | F | D | E | M | W |  |  |  | 
 |  | F | D | E | M | W |  |  | 
F | Stall |  | 
D | E | M | W |  | 
F | D | E | M | W | 
 | F | D | E | M | W
M | W
Load from the memory

## Slide 9: Memory Hierarchy
Main memory is large, but too slow
Small memory is fast, but cannot hold all required data
Solution: take the best of both and combine
Memory hierarchy provides visibility that memory is usually fast
L1
L2
L3
Cache
CPU
Main Memory
smallest, but fastest
slowest, but largest

## Slide 10: Real life example: Logistics
Your shop
Factory
Shop store
Storehouse
Large storehouse
The delay is decreased, but the cost is increased

## Slide 11: Why Does It Work?
Temporal Locality (Locality in Time):
  If an item is accessed, it will tend to be accessed again soon
  Example: code and variables in loops
→ Keep recently accessed data closer to the processor
Spatial Locality (Locality in Space):
  If an item is accessed, nearby items tend to be accessed soon
  Example: scanning an array
→ Move contiguous blocks closer to the processor
Locality + smaller HW is faster memory → hierarchy

## Slide 12: Localities are usually contradicting
Read of a large data array (data size >> cache size) has spatial locality, but no temporal locality
Read of a single variable has temporal locality, but no spatial locality
  for (size_t i = 0; i < N; ++i)
  sum += a[i];
  for (size_t i = 0; i < N; ++i)
  sum += i + *a;

## Slide 13: Cache implementation

## Slide 14: Cache: Main Idea
The cache holds a small part of the entire memory
  Need to map parts of the memory into the cache
Main memory is virtually partitioned into lines
  Typical block size is 32 to 64 bytes
  Blocks are aligned
The cache holds data by lines
  Only a subset of the blocks is mapped to the cache at a given time
Address of lines is used as a key
Memory
Cache
#line
#line
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
2 | 
91 | 
4 | 
5 | 

## Slide 15: Cache Lookup
Case 1: Cache Hit
  The requested line is in the cache
  The cache returns the requested line (fast)
2 | 
91 | 
5 | 
Memory
Cache
line#
line#
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
4?
4
hit
CPU

## Slide 16: Cache Lookup
Case 1: Cache Hit
  The requested line is in the cache
  The cache returns the requested line (fast)
Case 2: Cache Miss
  The requested line is not in the cache
  Need to fetch it from the main memory (slow) and fill the cache
  May need to evict another line from the cache to free space for the new one
91 | 
5 | 
Memory
Cache
line#
line#
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
93?
4
miss
2
93
93?
CPU

## Slide 17: Fully Associative Cache
Line may be mapped to any cache entry
  Lookup line in all entries
Address is partitioned to
  Offset within a line (byte#)
  Line # (so-called tag)
Each cache entry has a tag
  All tags are compared to the line# in parallel
  If one of the tags matches the line#, we have a hit
data
63
0
…
hit/miss
=
=
=
…
…
Tag
Array
Data
Array
64 | 5 | 0
Tag = line# | Offset | 
Address
0 | 
1 | 
… | 
511 | 

## Slide 18: Direct Mapped Cache
Line is mapped to the fixed entry only
  Lookup line in one entry
Address is partitioned to
  Offset within a line (byte #)
  Set (fixed cache entry #)
  Tag (works as a key)
Conflicts are possible
  If several lines are mapped to the same entry, only one can reside in the cache
data
0 |  |  | 
1 |  |  | 
… |  |  | 
511 |  |  | 
63
0
Tag Array
Data
Array
Address
64 | 14 |  | 5 | 0
Tag | Set |  | Offset | 
…
hit/miss
=
set#

## Slide 19: 2-Way Set Associative Cache
Conflicts are harmful → multi-ways cache is a solution
Each set holds two entries (way 0 and way 1)
  Each line can be mapped into one of two entries in the appropriate set
Address
64 | 13 |  | 5 | 0
Tag | Set |  | Offset | 
0 |  |  | 
1 |  |  | 
… |  |  | 
255 |  |  | 
63
0
Tag Array
Data Array
way #1
set#
0 |  |  | 
1 |  |  | 
… |  |  | 
255 |  |  | 
63
0
Tag Array
Data Array
way #0
set#

## Slide 20: 2-Way Set Associative Cache
Address
64 | 13 |  | 5 | 0
Tag | Set |  | Offset | 
0 | 
1 | 
… | 
255 | 
63
0
way #0
way #0
set#
hit/miss
=
0 | 
1 | 
… | 
255 | 
set#
way #1
=
63
0
way #1
Tag Array
Data Array
MUX
data
#lines = cache_size / line_size
#sets = #lines / #ways
offset_bits = log(line_size)
set_bits = log(#sets)
#lines = 32KB / 64B = 512
#sets = 512 / 2 = 256
offset_bits = log(64) = 6
set_bits = log(256) = 8