## Slide 1: Virtual memory
Oleg Ladin
01.03.2021

## Slide 2: Layers of Abstraction in Computer Science
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of this lecture

## Slide 3: Agenda
Virtual memory
Page table
TLB
Virtual memory HW optimizations

## Slide 4: Virtual Memory

## Slide 5: Memory management
Before: the whole machine for one program
  Resources are managed manually by the SW developer
  No “external” SW with unknown requirements
Now: multi-tasking
  It’s effective to share resources between processes
  Co-existence of many unknown processes cannot be planned
How multiple processes share memory?
  What if a process accesses memory of another process?
  What if process needs more memory and there is left?
  What if a new process is spawned?
static part
dynamic part
Text
Executable code
Heap
Dynamic memory allocation
Stack
Local variables in func. calls
Data
Initialized static variables
BSS (block starting symbol)
Uninitialized static variables
stack growth
heap growth
address 0
address N

## Slide 6: Virtual & physical memory
The virtual address space
  Perfect abstraction = contiguous and completely belongs to the process
  Visible to the programmer
  The physical address space
  The real computer memory (e. g. DRAM) used by multiple processes
  Hidden from the programmer by OS and HW
  How to map the virtual space to the physical one?

## Slide 7: Basic Idea of VM
  One process = one virtual address space
  Split virtual and physical spaces into blocks of fixed size (usually 4KB) – pages
  Only pages used by the process are stored in computer memory
    No need to place the whole virtual space
  Pages can be in physical memory or a disk
    Memory acts as a cache for the secondary storage – the disk
    Process may use more pages than physical memory can keep
Virtual Space
Physical Space
#page
#page
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
… | 
… | 
91 | 
92 | 
93 | 
… | 
… | 
2 | 
19 | 
40 | 
41 | 
Disk
#page
60 | 
122 | 

## Slide 8: Virtual memory advantages
Isolation of processes
  VM prevents them from illegal accessing the memory of one another
Illusion of large memory
  VM size can be bigger than physical memory size
Illusion of contiguous memory
  Programmers need not worry about where data is placed exactly
Dynamic memory growth
  Can add memory to processes at runtime as needed

## Slide 9: Page Table

## Slide 10: Page Table
  Contains the following information for each page:
  Is the page in memory or on the disc?
  A physical address of the page (if it is in memory)
  Was its data modified? → need for evictions
  Access rights (read-only, read-write, etc.) → security
  Each process has its own PT
  All complex tasks (initialization, misses, evictions, etc.) are performed by OS
  HW uses PT only to translate virtual addresses into physical addresses

## Slide 11: Translation
 | Disc or memory? | Modified? | Access Rights? | Physical page number
0 |  |  |  | 
1 |  |  |  | 
… |  |  |  | 
… |  |  |  | 
 | Disc or memory? | Modified? | Access Rights? | Physical page number
0 |  |  |  | 
1 |  |  |  | 
… |  |  |  | 
… |  |  |  | 
Page Table
63 | 11 | 0
Virtual Page Number | Page Offset | 
Virtual Address
31 | 11 | 0
Physical Page Number | Page Offset | 
Physical Address

## Slide 12: Page table structure
Implementation of a page table is defined by OS
Usually it is a multi-level table
  Accessing of final page table entry is a chain of loads (“walk”)
  Effective when pages are sparse in the virtual address space
63 | 11 | 0
Virtual Page Number | Page Offset | 
31 | 11 | 0
Physical Page Number | Page Offset | 
 | Level 1 Table
0 | 
1 | 
… | 
… | 
 | Level 1 Table
0 | 
1 | 
… | 
… | 
 | Level 2 Table
0 | 
1 | 
… | 
… | 
 | Level 2 Table
0 | 
1 | 
… | 
… | 
 | Level N Table
0 | 
1 | 
… | 
… | 
 | Level N Table
0 | 
1 | 
… | 
… | 
...

## Slide 13: Translation failures
The virtual address is invalid → “Segmentation fault” exception is raised
  When no PT entry were allocated for this virtual address by OS
The page is not in physical memory → Page fault
  HW saves the current state and gives control to OS
  OS detects the page causing the fault
  OS evicts some page, if no free pages left in physical memory
  OS loads the page from a disk to physical memory
  OS updates the PT entry (a physical address and “on disk?” bit)
  OS gives control back to HW

## Slide 14: Context protection
One process must not access physical memory of another process
  Each process has its own page table therefore
How to write to PT? CPU works in 2 modes at least
Kernel mode:
  entered by syscall
  has write access to PTs of all processes
  knows what physical addresses are
User mode:
  return from kernel mode by eret instruction
  operates only with own PT in a read-only manner

## Slide 15: TLB - Translation Lookaside Buffer

## Slide 16: TLB
  PT is too huge to be in HW → it is stored in memory
  There are multiple methods to compact it
  Each translation requires several memory accesses
  Needed for every load or store → too many!
  Data cache helps, but not much
  TLB caches recently used PT entries
  speed up translation
  typically 64 to 256 entries
  usually 2 to 8 way associative
  TLB access time is faster than L1 cache access time
Yes
No
TLB Hit ?
Access
Page Table
Virtual Address
Physical
Addresses
TLB Access

## Slide 17: PT + TLB + Cache
Yes
No
Access
TLB
Access
Page Table
In Memory
Virtual Address
Physical
Addresses
TLB
Hit ?
L2 Cache
Hit ?
No
L1 Cache
Hit ?
Yes
No
Data
No
Access
Memory
L2 Cache
Hit ?
Access
Cache

## Slide 18: Handling TLB miss
TLB miss can be handled by SW:
  Exception is raised, control is given to OS
  OS fetches a PT entry from memory and writes it into TLB
or by HW:
  Handled as a usual cache miss
RISC-V allows both, x86 uses HW, MIPS - SW

## Slide 19: TLB protection
Simplest solution — flush TLB on context switch
  Not optimal if “new” context switches back early
Performance-friendly solution — process id is a part of TLB tag
  Translate for different contexts simultaneously
  Safe: one context will not read TLB entries of other contexts

## Slide 20: HW optimizations

## Slide 21: Optimization 1: overlapped TLB & cache access
#Set is contained within the Page Offset
  The #Set is known immediately
  Cache can be accessed in parallel with address translation
  Once translation is done, match upper bits with tags
Limitation: Cache ≤ (page size × associativity)
Virtual Memory view of a Physical Address
0
Page offset
11
Physical Page Number
38
Cache view of a Physical Address
0
5
disp
tag
set
6

## Slide 22: Optimization 2: virtually-addressed cache
Address translation only done on a cache miss
Problem 1: two virtual pages mapped to the same physical page
    Must not reside in the cache together
    On a cache miss, use a reverse TLB to verify that no other cache line already in the cache mapped to the missed physical address
Problem 2: flush cache on context switch
    Alternatively: add process ID as part of the tag
Cache
TLB
Main
Memory
VA
PA
CPU
data
data

## Slide 23: Thank You

## Slide 24: Open questions: free discussion
What address should be used for store forwarding?
What address space should be used for prefetching logic?

## Slide 25: Meltdown
OS kernel keeps some of its data in the process PT
  Effective for exceptions handling
  Reading requires kernel privileges, but it still can be read speculatively:
  # speculative path after a conditional branch:
  lw $r1, 0x0($r2) # [$r2] is in kernel-space memory
  andi $r1, $r1, 0x1 # read the bit 0 (may be any)
  slli $r1, $r1, 0x40 # 0, if the bit is 0, else 0x40
  addi $r3, $r3, $r1
  lw $r4, 0x0($r3) # fill the cache with [$r3] or [$r3 + 0x40]
  # ...
  lw $r4, 0x0($r3) # measure exec. time of this instruction