## Slide 1: Control Hazards. Branch Prediction
Oleg Ladin
11 November 2019

## Slide 2: Refresher: Pipelined vs. Non-Pipelined implementation
F
D
E
M
W
PC
F
D
E
M
W
PC + 4
F
D
E
M
PC + 8
instructions
time
Sync signal
(clocks)
4ns
8ns
12ns
16ns
wait
F
D
E
M
W
wait
PC
PC + 4
PC + 8
wait
F
D
E
M
W
wait
wait
F
D
E
M
W
wait
time
Sync signal
(clocks)
4ns
8ns
12ns
16ns
Pipelined
Non-Pipelined

## Slide 3: Refresher: Forwarding + Hazard Detection Unit
Control
EX
M
WB
WB
M
WB
Hazard
Detection
Unit
0
D/E.MemRead
PC Write
0
m
u
x
1
F/D Write
Forwarding
Unit
1
m
u
x
0
0
m
u
x
B
1
2
0
m
u
x
A
1
2
Data
Memory
ALU
Register
File
Instruction
Memory
PC
D/E
E/M
M/W
F/D
Instruction
F/D.rs1
F/D.rs2
F/D.rd
D/E.rs1
D/E.rs2
D/E.rd
E/M.rd
M/W.rd
E/M.RegWrite
M/W.RegWrite

## Slide 4: Executing a BEQ Instruction (1)
beq x3, x2, 20;
0 or
4 beq x3, x2, 20 8 and 12 sw
16 sub
# if (x3 – x2 == 0)
# then PC  PC + SignExt(20)*2;
# else PC  PC + 4;
ALU
result
Add
result
Add
Shift
left 1
ALU
Control
RegWrite
Read reg 1
Read reg 2
Write reg
Write data
Read data 1
Read data 2
Register File
Sign
extend
D/E
E/M
M/W
MemRead
MemWrite
Address
Write Data
Read Data
Data
Memory
Branch
MemtoReg
4
Instruction
Memory
Address
Add
F/D
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
[19-15]
[24-20]
[31-20]
[11-7]
x3
x2
20
4
beq
8
8
and
Calculate branch condition
-
Calculate branch target

## Slide 5: Executing a BEQ Instruction (2)
beq x3, x2, 20;
0 or
4 beq x3, x2, 20 8 and 12 sw
16 sub
# if (x3 – x2 == 0)
# then PC  PC + SignExt(20)*2;
# else PC  PC + 4;
ALU
result
Add
result
Add
Shift
left 1
ALU
Control
RegWrite
Read reg 1
Read reg 2
Write reg
Write data
Read data 1
Read data 2
Register File
Sign
extend
D/E
E/M
M/W
MemRead
MemWrite
Address
Write Data
Read Data
Data
Memory
Branch
MemtoReg
4
Instruction
Memory
Address
Add
F/D
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
[19-15]
[24-20]
[31-20]
[11-7]
12
12
sw
4+SignExt(20)*2=44
8
and
beq
x3-x2=0

## Slide 6: Executing a BEQ Instruction (3)
beq x3, x2, 20;
0 or
4 beq x3, x2, 20 8 and 12 sw
16 sub
# if (x3 – x2 == 0)
# then PC  PC + SignExt(20)*2;
# else PC  PC + 4;
ALU
result
Add
result
Add
Shift
left 1
ALU
Control
RegWrite
Read reg 1
Read reg 2
Write reg
Write data
Read data 1
Read data 2
Register File
Sign
extend
D/E
E/M
M/W
MemRead
MemWrite
Address
Write Data
Read Data
Data
Memory
Branch
MemtoReg
4
Instruction
Memory
Address
Add
F/D
PC
0
1
m
u
x
0
1
m
u
x
0
1
m
u
x
Instruction
[19-15]
[24-20]
[31-20]
[11-7]
16
16 or 44
sub
12
sw
and
beq
  If the branch is taken the 3 wrong instructions get into the pipeline (they must be canceled somehow)
  => We are loosing 3 cycles after each taken branch!

## Slide 7: Decision 1: Stall pipeline
Do not execute instructions until branch condition is resolved
  3 cycles penalty for each branch
In average, every 5th executed instruction is a branch
  80% of program execution time is spent in loops
How much IPC would we loss?
CPI ideal (Clock per instruction) = 1
CPI real =
CPI ideal +
(% of branches)
× Penalty =
1.6
~20%
3
  37% slower => need to find something better
IPC real = 0.63

## Slide 8: Decision 2: Always Fetch Not-Taken
Execute instructions from the fall-through (not-taken) path as if there is no branch
If the branch is not-taken (~50%), no penalty is paid
If branch actually taken:
  Flush the fall-through path instructions before they change the machine state (memory / registers)
  Fetch the instructions from the correct (taken) path
Assuming ~50% branches not-taken on average. How lower it will be that ideal pipeline?
IPC real = 0.77
CPI real =
CPI ideal +
(% of branches × 50%)
× Penalty =
1.3
  23% slower => need to find something better

## Slide 9: Decision 3: Delayed Branches
Maybe ask the software (SW) to help?
  Need to change ISA to give it such possibility
Define branch to take place AFTER n following instructions
  Hardware (HW) executes n instructions following the branch regardless of branch is taken or not
SW puts in the n slots following the branch instructions that can be executed regardless of branch resolution
  Instructions that are before the branch instruction, or
  Instructions from the converged path after the branch
If cannot find independent instructions, put NOPs
Not Taken path
Taken path
Converged path
Branch
Only if it doesn’t depend on the instructions in T and NT paths
Only if it doesn’t define the branch condition

## Slide 10: Decision 3: Delayed Branches
Unfortunately, filling 1 delay slot is easy, 2 is hard, 3 is harder …
  Assuming we can effectively fill d% of the delayed slots
  For example, for d=0.6, we get CPI real = 1.2 (IPC = 0.83%)
Mixing architecture with micro-arch
  New generations requires more delay slots
  Compatibility issues between generations –> RISC-V has no delayed branches
  Still far from the ideal and mixing Arch and uArch is almost always not the best decision.
  Can we do something even better?

## Slide 11: Decision 4: Dynamic prediction
Dynamic branch prediction approach:
  As soon as branch is fetched (at IF stage) change the PC to the predicted path.
  Switch to the right path after the branch execution if the prediction was wrong.
It required complex hardware at IF stage that will predicts:
  Whether the instruction is a branch
  Branch taken or not
  Taken branch target
Structure performs such function is called Branch Target Buffer (BTB)
  In fact, it is organized exactly as a cache

## Slide 12: Using The BTB
PC moves to next instruction
Br taken ?
BTB Hit ?
Inst Mem gets PC
and fetches new inst
BTB gets PC
and looks it up
IF/ID latch loaded
with new inst
IF
ID
IF/ID latch loaded
with pred inst
IF/ID latch loaded
with seq. inst
yes
PC  PC + 4
no
no
PC  pred addr
yes
Branch ?
EXE
Correct target?
Flush pipe &
update PC
IF/ID latch loaded
with correct inst

## Slide 13: Using The BTB
MEM
WB
Flush pipe &
update PC
no
IF/ID latch loaded
with correct inst
yes
continue
continue
Corect
pred ?
Calculate br
cond & trgt
ID
EXE
Branch ?
yes
no
Update BTB

## Slide 14: Adding a BTB to the Pipeline
Mis-prediction detector
direction
target
predicted
flush
direction
target
actual
BTB
direction
target
branch IP
updates
predictions
direction
target
branch IP

## Slide 15: Adding a BTB to the Pipeline
Shift
left 1
ALUSrc
ALU
result
Zero
+
ALU
Control
ALUOp
RegWrite
Read
reg 1
Read
reg 2
Write
reg
Write
data
Read
data 1
Read
data 2
Register File
[31-20]
[11-7]
Sign
extend
ID/EX
EX/MEM
MEM
/WB
Instruction
MemRead
MemWrite
Address
Write
Data
Read
Data
Data
Memory
Branch
PCSrc
MemtoReg
4
+
IF/ID
PC
0
1
m
u
x
0
m
u
x
1
0
m
u
x
Inst.
Memory
Address
Instruction
BTB
1
2
pred target
pred dir
PC+4 (Not-taken target)
taken target
3
Mis-
predict
Detection
Unit
Flush
predicted target
PC+4 (Not-taken target)
predicted direction
−
4
address
target
direction
alloc/updt
Shift
right 2

## Slide 16: Performance of Dynamic Prediction
In case of correct prediction – loose nothing
In case of wrong prediction – flush the pipeline and restart from the correct PC
  Predict not-taken, actual taken
  Predict taken, actual not-taken
  Predict taken, but wrong target
Assuming P% correct prediction rate
  For example, if P = 85% (the modern predictors have 95%+)

## Slide 17: Methods of Branch Prediction

## Slide 18: Option 1: Backward Jump Predictor
If target PC is behind than branch PC, predict taken
    For the most of the cases that would be a backward jump of loop
    Loop branches are almost taken

## Slide 19: Option 2: Bimodal predictor
A saturating counter or bimodal predictor is a state machine with four states:
Advantages:
  Small – only 2 bits per entry in the BTB
  Predicts well branches with stable behaviour
Disadvantages
  Cannot predict well branches which often change their outcome:
    e.g. T, NT, T, NT, T, NT, T, NT, T, …

## Slide 20: Why does bimodal BTB work?
Branches are usually used in loops
  BTB trains on first iterations and predicts next ones correctly
Loops are not infinite, so once BTB will make a mistake
  It won’t affect next outer loop iteration!
while (cond1) // branch 1
{
while (cond2) // branch 2
{
// ...
}
}
Branch 2 history: T, T, T, T, T, T, NT, T, T, T, T, T, T, NT, T, T, T, T, T, T, NT...

## Slide 21: Option 3: Two-level adaptive predictor
1 0 0 1 0 0 1 0 0
0 0 0 0 0 1 0 0 0
past
future
present
History buffer
weakly
NT
strongly
NT
strongly
T
weakly
T
00
weakly
NT
strongly
NT
strongly
T
weakly
T
01
weakly
NT
strongly
NT
strongly
T
weakly
T
10
weakly
NT
strongly
NT
strongly
T
weakly
T
11
Prediction:
TRUE
Result:
FALSE
Pattern history table
Branch sequence:

## Slide 22: Option 4: Global Prediction
Often branch condition depends on previous control path (branch correlates with other branches)
The idea is to provide prediction per branch history
Branch history is kept as a hash of previous branches (block chain)
Drawbacks:
    # of possible “histories” is O(2N), so some filtering is mandatory
    Difficult to track and restore if pipeline is deep
There are Neural Network (Perceptron) Branch Predictors introduced

## Slide 23: Overview of alternatives

## Slide 24: Software Hints
Compiler may provide hints to branches (taken or not)
MIPS II provides “likely taken branches”, while old MIPS I branches are considered as “likely not taken branches”
RISC-V has no hints: BTB has low HW cost now
Cons:
    Irremovable (but small) penalty as target is unknown at IF
    Almost no value if CPU has a BTB

## Slide 25: Predication
The idea is to convert control hazard to data hazard
    Better if condition can’t be predicted by BTB
MIPS IV has 2 instructions: movn and movz
  movz $d, $t, $s <=> if (t == 0) d = s;
  movn $d, $t, $s <=> if (t != 0) d = s;
Example:
add $t0, $t1, $t2
bne $t0, $zero, cond
addi $t0, $t0, $1
cond:
div $t4, $t0
add $t0, $t1, $t2
addi $t3, $t0, $1
movn $t0, $t0, $t3
div $t4, $t0
x86 has a similar instruction cmov ARM has more advanced predication RISC-V has no predication

## Slide 26: Summary
Control hazards exist in pipeline
There are many ways to overcome them:
    do stalls
    speculatively fetch “always-no-taken” path
    use delayed branches
    use compiler hints
    use predication
The best way is dynamic branch prediction using:
    direction (forward/backward)
    local history
    recent local history
    global history

## Slide 27: Acknowledgments
These slides contain material developed and copyright by:
Lihu Rappoport (MAMAS/Intel), 234267, L2

## Slide 28: Thank You