## Slide 1: Practice 1 Combinational & Sequential Circuits
Korolev Kirill
5 October 2020

## Slide 2: SR Latch
reset
set
Q
!Q
R
!Q
S
Q
S | R | Qt-1 | Qt
0 | 0 | Q | Q
0 | 1 | Q | 0
1 | 0 | Q | 1
1 | 1 | Q | 0
Prohibited state
Symbol
Scheme
Truth table

## Slide 3: D Latch
Symbol
Scheme
Truth table
D | we | Qt-1 | Qt
D | 0 | Q | Q
0 | 1 | Q | 0
1 | 1 | Q | 1
D
we
Q
S
Q
R
!Q
Write enable
Data

## Slide 4: Task 1: Binary Decoder
A0 | A1 | D0 | D1 | D2 | D3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
A binary decoder is a logic circuit that converts a binary integer value to an associated pattern of output bits.

## Slide 5: Task 1: Binary Decoder – Answer
A0 | A1 | D0 | D1 | D2 | D3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
A binary decoder is a logic circuit that converts a binary integer value to an associated pattern of output bits.

## Slide 6: Task 2: Multiplexer
A multiplexer (or mux) is a device that selects one signal and forwards the selected input into a single line.
The entry wires are address bus and data buses
Address bus is connected via decoder
A0 | A1 | Out
0 | 0 | M0
0 | 1 | M1
1 | 0 | M2
1 | 1 | M3
M0
M1
M2
M3
A0
A1
Out

## Slide 7: Task 2: Multiplexer – Answer
A multiplexer (or mux) is a device that selects one signal and forwards the selected input into a single line.
The entry wires are address bus and data buses
Address bus is connected via decoder
A0 | A1 | Out
0 | 0 | M0
0 | 1 | M1
1 | 0 | M2
1 | 1 | M3
M0
M1
M2
M3
A0
A1
Out

## Slide 8: Single port 2MxN Memory Array
Memory array has 3 input signals and 1 output
Data buses are N bits wide (each chunk is N bits)
Address is M bits wide if 2M is array size
Memory
Array
address
input data
output data
M
N
N
Write enable

## Slide 9: Task 3: Single port 4x1 Memory Array
Data is stored in D latches
Use decoder and mux to select memory entry
Memory
Array
address
input data
output data
2
1
1
Write enable

## Slide 10: Arithmetic Logic Unit
ALU is a circuit that is able to perform different arithmetic and bitwise logical operations on integer binary numbers
ALU
Operand 1 (X)
Operand 2 (Y)
Opcode (I)
Result (out)

## Slide 11: Comparator
A comparator is a device that takes two numbers as input in binary form and determines whether one number is greater than, less than or equal to the other number
 | EQ | LEQ
A>B | 0 | 0
A==B | 1 | 1
A<B | 0 | 1
 | LE | EQ | GR
A>B | 0 | 0 | 1
A==B | 0 | 1 | 0
A<B | 1 | 0 | 0

## Slide 12: Edge-triggered D Latch (D flip-flop)
Don’t open for writing neither at we =0 nor at we =1
It is open for a very small amount of time when the write enable goes from 0 to 1
  It is a trigger asserted by the positive edge of write enable signal
Such types of triggers are mostly used to organize pipelined execution
D | we | Qt-1 | Qt
D
Q
clk (we)
D
0
Q
Q
D
1
Q
Q
D
↑
Q
D
D
↓
Q
Q

## Slide 13: Homework
Create scheme in Logisim – several variants
Will be announced via email

## Slide 14: Thank You