## Slide 1: RISC-V Single-Cycle implementation
Oleg Ladin
21 October 2019

## Slide 2: Layers of Abstraction in Computes Science
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topic of
this lecture

## Slide 3: Single-Cycle Implementation of RISC-V
Any ISA can be implemented in many different ways
The simplest one is single-cycle implementation:
  All operations are executed strongly sequentially
  Execution of an instruction is not started until the previous one is completely executed (no overlapping)
  All instructions take the same amount of time – a single cycle
For simplicity, only the following instructions (from RV32I) will be considered
Arithmetic | add, sub, addi
Data transfer | lw, sw
Control | beq

## Slide 4: Instruction Execution Cycle
Fetch Instruction by PC
Read registers
Process Calculations
Read/Write
Memory
Write registers
Update PC
Download instruction from the memory using value stored in the program counter (PC) register as an address.
Read values of registers which are pointed by the instruction as their source operands.
Execute an action encoded in the instruction (e.g. addition, subtraction, address calculation, etc.).
Write the result of the calculation into the memory or read the value using the address calculated on the previous step.
Write the result of the calculation or the value read on the previous step into the memory.
Update the program counter to the next instruction:
PC = PC + InstructionLength
Or it is a taken branch then:
PC = PC + BranchOffset

## Slide 5: Instruction Fetch
The CPU is always in an infinite loop, fetching instructions from memory and executing them
The program counter or PC register holds the address of the current instruction
RISC-V RV32I instructions are each four bytes long, so the PC should be incremented by four to read the next instruction in sequence
Add
4
Read
address
Instruction [31-0]
Memory
PC

## Slide 6: Executing reg-reg (R-type) Arithmetic Instructions
Read an instruction from the instruction memory by the address in PC
The source registers, specified by instruction fields rs1 and rs2, should be read from the register file
The ALU performs the desired operation
Its result is stored in the destination register, which is specified by field rd of the instruction word
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [19-15]
I [24-20]
I [11-7]
ALUop
funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
rd = rs1 (op) rs2

## Slide 7: Executing reg-imm (I-type) Arithmetic Instructions
I [24-20]
I [11-7]
Read an instruction from the instruction memory by the address in PC
The 1st source register, specified by instruction field rs1, should be read from the register file
The signed immediate is extended (from 12 to 32 bits) and directly transferred to ALU
The ALU performs the desired operation
Its result is stored in the destination register, which is specified by field rd of the instruction word
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [19-15]
ALUop
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALUop
Sign extend
I [31-20]
0
1
m
u
x
ALUSrc
funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
imm12[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
I
R
rd = rs1 (op) imm12

## Slide 8: Executing S-type Store Instructions
I [31-20]
Sign extend
Read an instruction from the instruction memory by the address in PC
The 1st source register (base address), instruction field rs1, is read from the register file
The 2nd source register (written value), instruction filed rs2, is read from the register file
The signed displacement is extended (from 12 to 32 bits) and directly transferred to ALU
The ALU calculates the effective address
The value is written into the memory by the effective address
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [19-15]
I [24-20]
ALUop
0
1
m
u
x
ALUSrc
Memory
Write
address
MemWrite
Write
data
I [11-7]
funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
imm12[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
offset12[11:5] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | offset12[4:0] |  |  |  |  | opcode |  |  |  |  | 1 | 1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
I
R
S
mem[rs1+offset] = rs2
Sign extend
I [31-20]
ImmSel

## Slide 9: Executing I-type Load Instructions
ImmSel
Read an instruction from the instruction memory by the address in PC
The 1st source register (base address), instruction field rs1, is read from the register file
The signed displacement is extended (from 12 to 32 bits) and directly transferred to ALU
The ALU calculates the effective address
The value is read from the memory by the effective address
The result is written in the destination register specified by field rd
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
I [19-15]
I [24-20]
ALUop
0
1
m
u
x
Memory
Write
address
Write
data
ALUSrc
MemWrite
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
ALUop
0
1
m
u
x
Memory
Write
address
Write
data
Read
address
ALUSrc
MemWrite
Read
data
1
0
m
u
x
MemToReg
I [11-7]
rd = mem[rs1+offset]
funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
imm12[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
offset12[11:5] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | offset12[4:0] |  |  |  |  | opcode |  |  |  |  | 1 | 1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
I
R
S
Sign extend
I [31-20]

## Slide 10: Executing S-type Branch Instructions (1)
Read an instruction from the instruction memory by the address in PC
The source registers, specified by fields rs1 and rs2, are be read from the register file
The signed offset is extended (from 12 to 32 bits) and shifted left by 1 (converted from half words to bytes)
The address of the instruction after the branch is calculated (= PC + 4)
The target address of the branch is calculated as (PC + (offset << 1))
The ALU compares the source operands (does subtraction) and generate the condition code (==, >, <, etc.)
The PC is update by the address of the instruction after the branch or by the target address depending on the branch opcode and the condition code
beq x3, x2, -0x0040
PC =
condition
target address
address of the next instruction
? ( PC + (-0x0040 << 1))
: (PC + 4)
((Reg[x3] – Reg[x2]) == 0)
depends on the branch opcode

## Slide 11: Executing S-type Branch Instructions (2)
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
Zero
I [19-15]
I [24-20]
ALUop
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 1
ALUSrc
MemWrite
MemToReg
0
1
m
u
x
PCSrc
Add
PC
4
The branch may or may not be taken, depending on the ALU’s Condition Code output (Zero here)
funct7 |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
imm12[11:0] |  |  |  |  |  |  |  |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | rd |  |  |  |  | opcode |  |  |  |  | 1 | 1
offset12[11:5] |  |  |  |  |  |  | rs2 |  |  |  |  | rs1 |  |  |  |  | funct3 |  |  | offset12[4:0] |  |  |  |  | opcode |  |  |  |  | 1 | 1
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
I
R
S
ImmSel
I [11-7]
Sign extend
I [31-20]
Add

## Slide 12: The Final Single-Cycle Data Path
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [19-15]
I [24-20]
ALUop
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 1
ALUSrc
MemWrite
MemToReg
0
1
m
u
x
PCSrc
Add
PC
4
ImmSel
I [11-7]
Sign extend
I [31-20]
Add

## Slide 13: Control Unit
The control unit is responsible for setting all the control signals so that each instruction is executed properly
The control unit needs different bits of an instruction
  7 (5 without reserved “11”) bits make up the instruction opcode
  3 + 7 (for some types) bits come from the instruction func3 and func7 fields
It also needs the Conditional Code (“zero”) output of the ALU
The control unit generates 7 of output, corresponding to the signals mentioned on the data path
Read
address
Instruction [31-0]
Memory
Read
address
Instruction [31-0]
Memory
RegWrite
ALUop
ALUSrc
MemWrite
PCSrc
ImmSel
MemToReg
Control
I [6-0]
I [31-25]
CondCode
I [14-12]

## Slide 14: Control signal table
sw and beq are the only instructions that do not write any registers
ALUOp depends on the instructions’ func field
The PCSrc control signal shows if instruction is taken branch
Operation | ImmSel | RegWrite | ALUSrc | ALUOp | MemWrite | MemToReg | PCSrc
add | x | Yes | Reg | 0010 | No | ALU | PC
sub | x | Yes | Reg | 0110 | No | ALU | PC
addi | i12 | Yes | Imm | 0010 | No | ALU | PC
lw | i12 | Yes | Imm | 0010 | No | Mem | PC
sw | s12 | No | Imm | 0010 | Yes | x | PC
beq | sb12 | No | x | 0110 | no | x | Br / PC

## Slide 15: Summary
A datapath contains all the functional units and connections necessary to implement an instruction set architecture
  For our single-cycle implementation, we use two-ported memory, register file, an ALU, some extra adders, and lots of multiplexers.
  RISC-V RV32I is a 32-bit machine, so most of the buses are 32-bits wide
The control unit tells the datapath what to do, based on the instruction that’s currently being executed
  The discussed processor has seven control signals that regulate the datapath
  The control signals can be generated by a combinational circuit with the instruction’s opcode and func fields as the input

## Slide 16: Simulation

## Slide 17: RISC-V Single-Cycle Data Path
Read
address
Instruction [31-0]
Memory
Read
register 1
Read
data 1
Registers
Read
register 2
Read
data 2
Write
register
Write
data
RegWrite
ALU
Result
I [19-15]
I [24-20]
ALUop
0
1
m
u
x
Read
address
Read
data
Memory
Write
address
Write
data
1
0
m
u
x
<< 1
ALUSrc
MemWrite
MemToReg
0
1
m
u
x
PCSrc
Add
PC
4
ImmSel
I [11-7]
Sign extend
I [31-20]
Add
RegWrite
ALUop
ALUSrc
MemWrite
PCSrc
ImmSel
MemToReg
Control
CondCode
Fetch
Decode
Execute
Memory
WriteBack
We are not going to model each component (e.g. multiplexer, adder) as it is done in RTL simulator

## Slide 18: Single-Cycle Implementation modeling
void RISCV::run(const string &trace, uint instr_to_run) {
// ... load trace
this->PC = startPC;
for (uint i = 0; i < instr_to_run; ++i) {
uint32 bytes = fetch(); // fetch() { return mem->read(PC); }
FuncInstr instr(bytes);
read_src(instr); // read_src() { instr->v_src1 = rf->read(instr->rs); …}
instr->execute(); // execute_add() { v_dst = v_src1 + v_src2; }
ld_st(instr);
wb(instr); // wb() { rf->write(instr->rd, instr->v_dst); }
PC = update_pc(instr);
}
F
D
E
M
W
class RISCV {
// storages of internal state
RF *rf;
uint32 PC;
Memory *mem;
void ld_st(FuncInstr &inst);
void wb(const FuncInstr &inst);
public:
RISCV();
void run(const string &trace, uint instr_to_run);
};

## Slide 19: Thank You