## Slide 1: Архитектура вычислительных систем
Организационная информация

## Slide 2: Цели и задачи курса (1)
MIPT-MIPS – это образовательный проект
Обзорное изучение компьютерной архитектуры
    Наибольший фокус на микроархитектуру процессоров
    Немного о системе команд MIPS, компиляторах и ОС
Навыки разработки в крупном командном проекте:
    Система контроля версий git
    Работа над open-source проектом в окружении GitHub
    Инфраструктура непрерывной интеграции
    Разработка через тестирование
    Документация и коммуникация: wiki, презентации, английский

## Slide 3: Цели и задачи курса (2)
MIPT-MIPS – это подготовка студентов к работе в реальных проектах компании Intel
Как попасть в Intel?
  Курс MIPT-MIPS (или другой курс лаборатории Intel)
  Кафедра «Микропроцессорные технологии» ФРТК
  Успешная стажировка в Intel с 3 по 6 курс
  Перевод на должность постоянного сотрудника
Участие серьезно повышает шансы вашего поступления на кафедру

## Slide 4: Мотивация
Для студентов:
  Самообразование и самоопределение
  Уникальные знания (аналогичных курсов нет не только в МФТИ, но и в других российских университетах)
  Поступление на кафедру → стажировка в Intel → работа в Intel
  Стипендия (максимальная стипендия > 10000 руб. в семестр)
Для преподавателей:
  Волонтёрство: никакой материальной заинтересованности
  Опыт управления проектом
  Обновление и расширение знаний

## Slide 5: Теоретические занятия
  Время: по средам, 17:05–18:30
  Место: 108 РТ
  Язык: текст презентаций – английский, материал читается на русском
  Тематика: общее устройство микропроцессорных систем

## Slide 6: Контроль успеваемости (тестирование)
  Когда: в конце семестра
  Тематика: весь пройденный за семестр материал
  Структура: развернутые ответы
  Длительность: одно занятие
  Язык: вопросы и ответы на русском языке

## Slide 7: Критерии оценки студента
Формула расчета рейтинга успеваемости:
    Посещаемость — 10% Результаты тестирования — 30% Практическая работа — 60%
  При поступлении на кафедру учитывается «общее впечатление»: мотивированность, аккуратность, исполнительность, креативность и т.д.
  Преподаватели не решают, какие студенты будут взяты на кафедру (стажировку). Финальное решение принимает менеджер компании.
  Обучение на проекте не гарантирует поступления на кафедру!

## Slide 8: Связь
Связь с преподавателями поддерживается очно и через e-mail
Объявления будут рассылаться через почтовую рассылку
Разрешается использовать только адреса @phystech.edu
  Легко установить отношение между адресом и именем человека
  Трудно ошибиться при в написании адреса
Общение ведётся на английском языке
  Нет необходимости перевода, если ваша проблема выходит за рамки проекта
  Увеличивает ваше знание английского

## Slide 9: Дисциплина
Пропуск занятия возможен, но крайне нежелателен.
    О пропуске лучше предупреждать за несколько дней.
Не забывайте проверять почту!
    Предполагается, что вы проверяете почту хотя бы раз в сутки.
    На письма, которые требуют какого-то действия, лучше отвечать сразу.
    Если вы не можете сделать то, что от вас требуется сразу, то просто напишите, когда вы будете готовы начать эту задачу.
Соблюдайте внутренние правила работы
    Делайте все правильно с первого раза, а не ждите пока вас поправят.
Все эти правила не относятся к преподавателям 
    Отнеситесь к этом с пониманием: вас много, а нас меньше

## Slide 10: Layers of Computer Science ISA and uArch levels
Pavel Kryukov
19 September 2018

## Slide 11: Acknowledgements
These slides contain material developed and copyright by:
Krste Asanovic (MIT/UCB), CS152-L1
David M. Koppelman (LSU), EE4720-L1

## Slide 12: Literature
Computer Organization and Design: The Hardware/Software Interface, Patterson D.A., Hennessy J.L., 3rd Edition (Eng) — the main book for this course. It contains all that you need to know about the computer architecture and MIPS ISA.
Computer Architecture: A Quantitative Approach, Hennessy J.L., Patterson D.A., 4th Edition — the classic book about state-of-the-art high-performance computing microarchitectures.

## Slide 13: What is this course about?
The shortest answer is about Computer Architecture
Computer architecture is the design of the abstraction layers that allow us to implement information processing applications efficiently using available manufacturing technologies
Ok… but what is it?
Application
Physics
Decision: create many layers with standardized interfaces
Issue: the gap is too large to cross it over in one step

## Slide 14: Layer 1: Application
The general tasks: money accounting, text editing, music/video encoding, games etc.
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
Excel
Overwatch
Photoshop

## Slide 15: Layer 2: Algorithms
High-level math methods to perform the task: quick sort, search in graphs, compression, signal encoding etc.
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
JPEG
LZ77
Dijkstra
FFT

## Slide 16: Layer 3: Programming language
Representation of algorithms in formal languages that can be translated to “machine language”
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
C++
Java
Python

## Slide 17: Layer 4: Operating system
Manages computer resources and provides common interface for user programs
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
Linux
FreeBSD
Windows

## Slide 18: Layer 5: Instruction Set Architecture
Definition of “machine language” (commands) and available hardware structures/mechanisms
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
x86
MIPS
RISC-V

## Slide 19: Layer 6: Microarchitecture
High-level definition of hardware structures and operations: caches, buses, registers, pipeline, etc.
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
Core™
Pentium®
Atom®

## Slide 20: Layer 6: Gates/RTL
Detailed definition of hardware: floor plan, wires, signal distribution, etc
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
Latches
Flip-flop
Gate

## Slide 21: Layer 7: Circuits
Structure and operation of base hardware elements: transistors, electricity effects
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
Transistors
Voltage
Current

## Slide 22: Layer 8: Physics
Low level physics effects
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
Semiconductor
Electron
Diffusion

## Slide 23: Layers of Abstraction
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Hardware (HW)
Software (SW)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
HW/SW interface
Computer Science
(CS)
Electrical Engineering
(EE)

## Slide 24: Course focus
We will focus our attention mostly on the microarchitecture, but also look through the ISA and the HW levels
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer
Circuits
Physics
The most focus is here

## Slide 25: Performance, Power, Cost

## Slide 26: Basic Design Tradeoffs
All three are very important
It is extremely hard to create a feature that improves all factors
Different products (mobile, desktop, etc.) require different balance
Performance
(speed)
Cost
(complexity, area)
Power
(energy consumption and dissipation)

## Slide 27: Performance
What does performance depend on?
Golden rule of CS

## Slide 28: Increasing Performance
How can we increase it?
Better SW: algorithms, optimizations, ISA, etc.
Better design: faster circuits, smaller transistors, etc.
Better uArch: pipelining, caching, prediction, etc.

## Slide 29: Power
Why is power important?
  Less power -> smaller battery -> smaller/cheaper devices
  Less power -> less money for electricity
Power Wall is reached
  Cooling systems cannot dissipate more heat
  We cannot spend more power even if we want
Nuclear reactor? No, power supply for a large data center

## Slide 30: Cost
Fixed Cost (RnD)
    Independent of volume (i.e., number of units made/sold)
    Examples: design time and effort, mask generation, etc.
Variable Cost (manufacturing/production)
    proportional to volume
    Examples: silicon processing, packaging, test
    Most of these related to chip area
The larger chip size the large production cost
    Less chips on one wafer
    Larger probability of error

## Slide 31: ISA and uArch

## Slide 32: ISA and uArch
Instruction Set Architecture (ISA) is a precise definition of:
  computer instructions and features
  mechanisms like procedures, interrupt/exception handler, etc.
  some structures
An agreement between a programmer and an engineer:
    It’s all programmer needs to program machine.
    It’s all hardware designer needs to design machine.
Microarchitecture (uArch, implementation) is an organization and features of Hardware that executes instructions and support features defined in the ISA.

## Slide 33: ISA and uArch
What a typical ISA defines
    Data Formats. (Integer, Floating Point, Vector/Packed)
    Instructions. (Operations, encoding, etc.)
    Registers and Memory Organization.
    Interrupts, exceptions, and traps.
    Implementation-Dependent Features. (Memory control, custom features.)
What a typical uArch defines (not included into ISA)
    Memory hierarchy organization (caches, buses, etc.)
    Pipeline (forwarding, branch prediction, etc.)
    Out-of-order executions … and many others.
the programmer-visible state
they change the state

## Slide 34: Example: MIPS
An example of a RISC ISA.
    Designed for easy programming and implementation.
    Short and simple, but fast instructions → programs are larger than others, but IPC is higher.
The main aim was to take advantages of pipelined execution
    Pipeline was not specified in ISA, but ISA developers tried to simplify its implementation in uArch.
Implementations:
    The first one is R2000 (1986)
    Later: R3000A (PlayStation), VR4300 (Nintendo64), R4000 (PSP), R5900 (PlayStation 2)
    Currently it is widely used in high-performance embedded systems, like MobileEye
One moment MIPS seemed to be overcome Intel IA-32...
  It didn’t happen because Intel’s uArch was significantly better and could compensate the drawback of IA-32

## Slide 35: Example: RISC-V
Pronounced “rick-five”
Another example of a RISC processor
  Designed to fix MIPS design errors:
    Well-defined instruction subsets
    No obsolete instructions
    Royalty-free
  Implementations and toolchains are designed in universities
  Potentially #1 competitor to ARM in microcontroller markets

## Slide 36: Example: IA-32 and x86-64
An example of CISC ISA
  Designed for laconic code and simpler assembler programming
  CISC advantages are not important now
Became de-facto standard in 90-2000s because of Intel CPU quality
Incrementally extensions: MMX, SSE, AVX etc.
Polished toolchains and documentation

## Slide 37: Data Formats
In the memory all including data and program code is presented as binary numbers:
Data representation:
    Sizes: 8-b Bytes, 16-b Half words, 32-b words, 64-b double words
    Formats: signed/unsigned integer, signed/unsigned floating point
0000 0010 | 0011 0010 | 0100 0000 | 0010 0000
add $t0, $s1, $s2
0x2012620
=
=

## Slide 38: Memory addressing
Memory (MEM) is a concept of a storage for programs and their data
    It is a part of programmer-visible machine state (fully controlled by a programmer)
    It can be though as an linear array of Bytes.
    Data can be read or written into this storage using an index which is called memory address.
    The size of the memory is equal to Bytes, where N is the maximal number of bits that can be encoded in a memory address.
    Usually, there is no separate memory for code or data. They are stored together in the same space.
00100100
…
…
…
…
…
…
8 bits = 1 Byte
0
1
2

## Slide 39: Big and Little Endian
  Historically numbers are being written from the right to the left (the most significant digit is on the right):
  However, we enumerate elements in an array (and most other things) from the left to the right:
  The question: if we put an value of two bytes (e.g. 256) at the beginning of the array where the most significant byte will be? In element 0 or element 1?
Decimal 537 = 7* + 3* + 5*
Binary 1101 = 1* + 0* + 1* + 1*
…
…
…
…
…
…
…
0
1
2
Decimal 537 = 7* + 3* + 5*
Binary 1101 = 1* + 0* + 1* + 1*

## Slide 40: Big and Little Endian
  The answer: it depends on the endianness of the ISA
Decimal 256 = Binary 0000 0001 | 0000 0000
Big Endian
Little Endian
15
8
7
0
Decimal 256 = Binary 0000 0001 | 0000 0000
Decimal 256 = Binary 0000 0001 | 0000 0000
Most significant byte
Least significant byte
0
1
2
00000001
00000000
7
0
15
8
0
1
2
00000000
10000000
15
0
8
7
  Most of the modern ISAs are little-endian

## Slide 41: Registers
Registers are fast, but small (vs. memory) data cells
    A great amount of registers are included into programmer-visible machine state (fully controlled by a programmer):
        Program counter (PC) stores the address of the currently executed instruction
        General Purpose Registers (GPR) is used to store intermediate calculations.
        There are many examples of other registers (Flags, Control Registers, etc.)
    The GPR can be thought as an array of elements indexed by numbers of registers encoded in instructions.
    In general, the maximum number of the GRP is equal to , where N is the maximal number of bits that can be encoded in a instruction as a register number.

## Slide 42: Basic RISC operations
Move: set a register to constant value or value of other register
Load: move a value from memory/IO to register
Store: move a value from register to memory/IO
Arithmetic: addition, subtraction, multiplication, division
Logic: conjunction, disjunction, negation, exclusive disjunction
Comparison: equal, not equal, less, greater, less than etc.
Direct unconditional branch: jump directly to some code
Direct conditional branch: jump to some code conditionally (if/then)
Indirect branch: read address from register and jump to it (switch/case, returns)
System calls: call for resource managements by OS

## Slide 43: Summary
What a typical ISA defines:
    Data Formats: bit width, endianness
    Registers and memory organization
    Instructions — ‘rules’ to change registers and memory
    Interrupts, exceptions, system calls, and traps.
  But what does uArch define?
    We’ll discuss it as soon as we look to the lower CS levels — gates, circuits, physics

## Slide 44: Thank You